Overall Problem:

We have a need to drive a Bistable Rotary Solenoid to control a robot arm.

Components in the Solution:

- TI, DRV8801 motor driver (DRV8801EVM board)

- Atmel processor

- Bistable Rotary Solenoid

Overall Design

The goal is to drive the bistable rotary solenoid CW and CCW using a PWM signal. The Enable pin is supplied a with a PWM signal. Phase signal is use to control CW and CCW. For this experiment the mode1 and mode2 pins are 0 and 1 respectively.

- Channel 1 - Out+

- Channel 2 - Out-

- Channel 3 - Enable (PWM signal)

- Channel 4 – Phase

In this scenario I am expecting Out- to have the compliment of the PMW signal seen on Out+. Base on the limited information I hope you can shed some light on the problem. If you need more information please feel free to e-mail me at mahendra.gunawardena@omnyx.com or call me at 765-271-1638.

Analysis done on 10/21/2011

Phase Low, PWM signal on enable, Mode1 Low, Mode2 high

Added following condition before Phase was change to high on 10/21/2011

Phase Low, 0% PWM signal on enable, Mode1 High, Mode2 Low (Braking)

Phase High, PWM signal on enable, Mode1 Low, Mode2 high

Above scope plot represents the Solenoid CW and CCW. In the above scope plot the Solenoid is disconnected thus there is no load. On channel 2 when the phase is low complement of channel 1 is expected instead the result is a solid high. Both segments of scope plots are expanded below.