## Slide 1: rePaper BoosterPack + LaunchPad Example
www.ti.com/launchpad
Notes: 9AM – 10:15 Intro & Hardware
10:15 – 10:30 Break
10:30 – 11:30 Software
11:30 – noon Q & A
Noon to 1 Lunch
1 – 3 Workshop first half
3 – 3:15 Break
3:15 – 4:15 Workshop second half

## Slide 2: LaunchPad is Modular Hardware
MSP430
Tiva C
C2000
Hercules
LaunchPad kits featuring TI MCUs & standardized BoosterPack interface
MCU + RF SoC LaunchPads coming soon…
CC3101 WiFi + ARM MCU (ECS)
CC26xx RF + ARM MCU (LPRF)
Wireless BoosterPacks enabled by TI transceivers
Coming soon:
CC3100/CC3101 BoosterPack
CC26xx BoosterPack
CC2541s BoosterPack
CC1300 BoosterPack
Additional BoosterPacks for building applications, demos & rapid prototyping
Sub-1GHz
NFC/RFID
WiFi
ZigBee
BLE
(CC110L)
(TRF7970A)
(CC3000)
(CC2530)
(CC2541)
Bluetooth
(CC2567)
Thermocouple BoosterPack
(ADS1118)
MEMS Temp Sensor BoosterPack
(TMP006)
ePaper Display BoosterPack
(RePaper)
LiPo Battery
BoosterPack
(BQ fuel gauge)
SensorHub
BoosterPack
(various sensors)
Ultra-Low Power ePaper Display
ePaper BoosterPack from Pervasive Displays
- 1.44”, 2.0” & 2.7” displays available
MSP-EXP430G2
LaunchPad

## Slide 3: In this lab…
We are going to use the MSP-EXP430G2 LaunchPad & ePaper BoosterPack from Pervasive Displays Inc.
We will use CCS to program an example application, which will allow us to send text, images & other information to the ePaper BoosterPack
We will use the EPD Kit Tool from Pervasive Displays, which allows us to interface with the ePaper display using a PC-side interface
Finally, we will save the binaries for this particular example for future use

## Slide 4: MSP430G2 LaunchPad + ePaper BoosterPack
Hardware required:
Functional Block Diagram:
  Featuring eInk display (Pervasive Display)
  SPI interface
  Only requires power during image change
+
MSP-EXP430G2
LaunchPad
Pervasive Display
eInk BoosterPack
=
Ultra-Low Power ePaper Display
eInk
Display
SPI
Serial Flash
Power
Mgmt
MCU

## Slide 5: Let’s get started!
Plug the ePaper BoosterPack to your MSP430 LaunchPad. If you are using the MSP-EXP430G2 LaunchPad, be sure that the UART jumpers are in the right position as shown in the image.
In this example, we will use an existing example created in Code Composer Studio
Plug LaunchPad into your computer using mini-USB cable

## Slide 6: Let’s get started!
Open up Code Composer Studio
Create a new Workspace called “LaunchPadWorkshop”

## Slide 7: Import the ePaper BoosterPack example
Project > Import Existing CCS Eclipse Project :
  “[ROOT]/LaunchPad_Workshop/BOOSTERPACKS/ePaper_BosterPack/CCS_Demo_eInk”
Click “Finish” to import the project

## Slide 8: Configure the code for your display
This code will work on various ePaper displays from Pervasive Dislpays, Incorporated.
We need to tell the code, which display we are using by editing image_data.h
This file is located at:
EPD Extension Board > src > image_data.h
We need to set #define to the right value depending on the eInk display you are using:
  USE_EPD_TYPE USE_EPD144
  USE_EPD_TYPE USE_EPD200
  USE_EPD_TYPE USE_EPD270

## Slide 9: Compile the project
Double-click “EPD Extension Board” in the Project Explorer window to make it “Active”
Click on the green “DEBUG” to compile the project & load it into your LaunchPad
If a “ULP Advisor” window pops up, ignore & click “Proceed”
This will now compile your project & switch you to the DEBUG view of CCS

## Slide 10: Run the example code!
Once your code is compiled & loaded into the MSP430 device, click on the “Run” button to start executing the code.
At this time, your LaunchPad & ePaper BoosterPack is ready to receive an image to be sent from the computer!

## Slide 11: The ePaper Display Kit Tool
To send images to your LaunchPad, we will use a PC-side tool called “EPD Kit Tool”
The installer for this tool is available in your workshop folder:
[ROOT] / LaunchPad_Workshop / BOOSTERPACKS / ePaper_Boosterpack / EPD Kit Tool
Double-click the installer & run through the installation.
Once installed, run the EPD Kit Tool software from the location you installed it.

## Slide 12: The EPD Kit Tool
Be sure your LaunchPad & ePaper BoosterPack is plugged into USB
Scan for your LaunchPad by pressing the “Scan” button.
Be sure to select the right EPD size!!!
This should also correspond to the size you specified in the code.
Press “Connect”

## Slide 13: The EPD Kit Tool
Once connected, you will see there are 4 tabs:
  Drawing
  SlideShow
  ASCII
  Others
Let’s try the “Drawing” tab.
When you click “Load Image”, you will be able to browse for example images. Be sure to choose images that have the right dimensions/size
Once you select an image, press “Open”
This should trigger the image to be sent to your LaunchPad!

## Slide 14: The EPD Kit Tool
The EPD Kit Tool offers various modes.
The “Drawing” tab allows you to draw images, lines, squares & circles on the ePaper display.
The EPD Kit Tool accepts mono-color Bitmap (BMP) image files. The pixel dimension of the picture is dependent on the ePaper display you are using.
For 2.7” displays, the pixel dimensions are 264px x 176px
The “SlideShow” tab allows you to cycle several images in an automatic slide show.
The “ASCII” mode allows you to send text to your ePaper display.
The “Others” tab allows you to do a few other things with your BoosterPack.
NOTE: ePaper only needs power when changing the contents of the screen!
Once you have an image on the screen, remove power from the LaunchPad.
The image should remain on the ePaper display!

## Slide 15: Let’s save the binary for this example
Let’s keep the project binaries (.hex file) so that we can quickly flash this example for customer demos in the future!
You can find the .hex file of this project in the “Debug” folder in the CCS Project Explorer window
Right-click & copy that file.
We will paste it into the following directory for later use:
[ROOT]/LaunchPadWorkshop/BOOSTERPACKS/ePaper_Display/EXAMPLE_BINARIES/
Now that we have the binaries saved, we can use CCS UniFlash to load it into your MSP430 LaunchPad at any time
Give your new binary file a descriptive file name

## Slide 16: Helpful Links
www.ti.com/launchpad
http://www.pervasivedisplays.com/kits/ext_kit
www.ti.com/ccs