## Slide 1
[SERDES Interface Block diagram]
Distance from Target : 40~50m, transmission speed is expected to 500Mbps.
Interface cable : connected to CAT5e,STP cable.
Schematic is referred to the Application Note AN-1909.
(DS15BA101 and DS15EA101 Enable Long Reach Applications for Embedded Clock SER/DES)
And referred to DriveCable02EVK User Manual.
Serializer : DS92LV1023EMQ (TI)
Deserializer : DS92LV1224TMSA (TI)
High-speed Differential Buffer : DS15BA101SDE (TI)
Adaptive Cable Equalizer : DS15EA101SQ(TI)
Clock Buffer : LMK00105SQE (TI)
Serializer
DS92LV1023EMQ
Deserializer
DS92LV1224TMSA
TX_DATA 5~6 bit
RX_DATA 3 bit
High-Speed
Differential Buffer
DS15BA101SDE
LVDS
Cable
Extender
DS15EA101SQE
TARGET
CLOCK
Buffer
LMK00105SQE
Input Clock 50MHz
50MHz
CAT5e, STP Cable
CAT5e, STP Cable