## Slide 1
Send WR_CAN_STBY with CANWU=1, VSOUT1_EN=1 and 100ohm/100uF Load
100ohm and 100uF load is connected at VSOUT1 to reach nominal voltage delayed from VDD3/5.
RES
VSOUT1
VDD3/5
Device State behavior (Please playback following file.)
1ms
Evaluation result using TPS65381EVM |  |  |  |  |  | 
Condition: |  |  |  |  |  | 
VSOUT1_EN=1 |  | (100ohm and 100uF load is connected at VSOUT1 to reach nominal voltage delayed from VDD3/5.) |  |  |  | 
NO_SAFE_TO=1 & SAFE_LOCK_THR=0 |  |  |  |  |  | 
CANWU=1(Fro all procedure) |  |  |  |  |  | 
I changed the state according to "State Number" 1->2->3->4->5->6. |  |  |  |  |  | 
State Number | State | Applied trigger to cause state change | DEV_ERR_CNT | ABIST_UVOV_ERR | ERROR_PIN_FAIL | WD_FAIL
1 | ACTIVE |  | 0 | 0 | 0 | 0
 |  | Send WR_CAN_STBY |  |  |  | 
2 | SAFE |  | 1 | 0 | 0 | 0
 |  | Send WR_CAN_STBY |  |  |  | 
3 | SAFE |  | 2 | 1 | 0 | 0
 |  | Send WR_CAN_STBY |  |  |  | 
4 | SAFE |  | 3 | 0 | 0 | 0
 |  | Send WR_CAN_STBY |  |  |  | 
5 | SAFE |  | 4 | 0 | 0 | 0
 |  | Send WR_CAN_STBY |  |  |  | 
6 | SAFE |  | 4 | 0 | 0 | 0