## Slide 1: Open GUI

## Slide 2: Click on magnifying glass to scan for devices

## Slide 3: Highlight the device, right click on it, then select “apply template from file”. Select file called “FT4232H_custom_tsw1400.xml

## Slide 4: Click on “USB String Descriptors”. Check then Uncheck Auto Generate Serial No.

## Slide 5: A new serial number will now be present. Click on lightning bolt to the right of the magnifying glass to start programming mode.

## Slide 6: Click on “Program” to program device.

## Slide 7: Close programming window. Click on magnifying glass to verify that the part was programmed with the new serial number.

## Slide 8: When doing a second board, just click on magnifying glass and uncheck “Auto Generate Serial No.” then program device.