Details of Power Supply-

- VCC = +5V, VEE = -5 V, Analog ground is represented as AGND, VA = +5 V same as VCC with respect to AGND, VBD = 5V_B=5 V  with respect to BGND (digital ground)

- AGND and DGND shorted on one point using Jumper J10.

- REFOUT  connected to REFIN and BUSY connected to MXCLK.

- BUS18_16 and BYTE are permanently grounded (logic low level)to get 18 bit output, we are reading upper 16 bits leaving lower two LSB’s using DSP. Buffer is connected at the outputs of the ADC.

- C1 is permanently high (logic high), C2 and C3 are permanently low (logic low) and AUTO is permanently high for auto mode.  With this connection we would like to use two chnnels in auto mode.

- CS and RD are toggled using DSP..

- Start of conversion (Active low) is generated (a pulse) using DSP.

We are getting

3.76 Volt on internal reference output pin 11,

3.76 Volt on BUF-REF pin15

and  1.88 Volt on VCMO  pin 14

but as per datsheet these should be 4 volt , 4 volt and 3 volt respectively.

Please clarify????

When we give start of conversion on pin 2 we get busy signal but we get

fixed digital data either 0 or 5AD2 on giving read signal for all the

inputs -4 volt to +4 volt).

We do not understand where is problem. Pl provide technical support for

getting correct digital outputs. Due to this problem our work is affected

very badly Please provide technical help at the earlist.