## Slide 1: Profiling (with CCS)
Embedded Development Tools

## Slide 2: "Program analysis tools are extremely important for understanding program behavior. Computer architects need such tools to evaluate how well programs will perform on new architectures. Software writers need tools to analyze their programs and identify critical sections of code. Compiler writers often use such tools to find out how well their instruction scheduling or branch prediction algorithm is performing..." -- (ATOM, PLDI, '94)

## Slide 3: What is Profiling?
Dynamic program analysis that can measures relative statistics on your application
  Profiling analyzes program execution and can show where your program is spending its time
Profiling is achieved by instrumenting either the program source code or its binary executable form using a tool called a profiler
  A number of different techniques may be used by profilers, such as event-based, statistical, instrumented, and simulation methods
Profilers can use a wide variety of techniques to collect data, including:
  Hardware interrupts, code instrumentation, instruction set simulation, operating system hooks, and performance counters
Notes: 3

## Slide 4: Why Profile?
Performance is critical for any program, but especially so for embedded programs
  Most common use of profiling information is to aid program optimization
80/20 rule: 80% of the time is spent in 20% of the code
  Hard to identify that 20% as programs continue to grow in size and complexity!
Profiling helps to identify that 20%
  Where is the most time being spent?
  Which functions takes the most time?
  Which functions are called the most?
Profiling helps reduce the time it takes to identify and eliminate performance bottlenecks
Notes: 4

## Slide 5: Profiling with CCS

## Slide 6: Non-Instrumented

## Slide 7: CCS Function Profiler
Provides Function Profiling information for all functions
Data Collection
  Simulator support is provided by collecting PCDT (PC discontinuity (branch)) data
  Hardware support is provided by setting breakpoints on each function entry/exit point and reading a counter on the target
Supported on:
  Simulation: ARM, C55x, C6x
  Hardware: ARM7/9, C55x
Notes: 7

## Slide 8: CCS Function Profiler
Pros
  Easy to use
  Works “out of the box” (no special tools or setup needed)
  Very effective on simulator targets
    Non-intrusive
    Good visibility
Cons
  Breakpoint based on HW (halt target to read the counter)
    Intrusive (constant halts due to breakpoints)
    Unusable for programs in flash due to limited number of HW breakpoints
  Not supported on all devices or simulators
    Very limited support for HW targets
Notes: 8

## Slide 9: CCS Function Profiler
Tools -> Profile -> Setup Profile Data Collection
Select from a variety of events to profile.
NOTE: Available events vary per target
Both inclusive and exclusive counts are available

## Slide 10: CCS Code Coverage Tool
Provides Line and Functional coverage information for a program after its execution has completed
Data Collection
  Instrumentation and collection handled by the simulator non-intrusively
Supported on:
  C6x simulators only
Pros
  Easy to use
  Works “out of the box”
  Non-intrusive
  Good visibility
Cons
  Supported only on C6x simulators
Notes: 10

## Slide 11: CCS Code Coverage Tool
Editor highlighting of line coverage data

## Slide 12: View Function and Line Coverage Results
Function and Line Coverage and Profile results

## Slide 13: CCS Profile Clock
A counter used to count events (usually cycles) when executing program from point A to point B (next time program is halted)
Data Collection
  Enables and reads a counter on the target and then stores value on to a local buffer on the host (CCS)
    The counter used varies from target to target
    Usually the same counter that can be used by the CCS function profiler
Supported on:
  (Almost) all targets
    Very few targets do not support the profile clock (Cortex-Mx)
Notes: 13

## Slide 14: CCS Profile Clock
Pros
  Easy to use
  Supported on (almost) all targets
Cons
  Only useful for basic use cases
    Can only count events for one range at a time
  Requires an emulation resource (can be an issue when emulation resources are lacking (HW breakpoints, watchpoints, etc)
Notes: 14

## Slide 15: CCS Profile Clock
Run -> Clock -> Enable
Run -> Clock -> Setup
  Choose event to count (default is CPU cycles)
    Available events vary with the target (simulators and C6000 HW support the most events)
Notes: 15

## Slide 16: Processor Trace
Provides profiling information for a program execution using processor (CPU) trace
Data Collection
  PC discontinuity, data and event trace captured in an on-chip memory buffer (ETB) or a external dedicated trace receiver (XDS560v2 Pro Trace Emulator)
    ETB buffer size: 2-8 KB (10K – 30K processor lines)
    XDS560v2 Pro Trace buffer size: 2 GB (1M – 1G processor lines)
Notes: 16

## Slide 17: Processor Trace
Pros
  Great visibility into the program execution
  CCS data visualization and analysis tools can process and display trace data in a number of useful formats
    Exclusive Function Profile data
    Line profiling data
    Code Coverage data
  No additional hardware needed to use the ETB
Cons
  Only supported on select devices with an ETB or targets (device and board) that can support XDS560v2 Pro Trace
  Limited window of visibility when using the ETB due to limited buffer size
  XDS560v2 Pro Trace:
    Expensive (~$3500 USD)
    Supported by a limited number of C6x devices
    Additional pins on the board for trace data
Notes: 17

## Slide 18: Processor Trace - Trace Viewer
Function profiler
Function call graph
Source code tracking
Source
code
correlation
Advanced
data
navigation
features
Notes: For devices that have trace connected to both ETB and pins

## Slide 19: Processor Trace – Function Profiler
19
Generate exclusive function profiling information from processor trace data

## Slide 20: System Trace
Trace capability that monitors synchronization and timing between cores and on-chip peripherals
Data Collection
  Event (STM) messages captured in an on-chip memory buffer (ETB) or a external dedicated system trace receiver (XDS560v2 STM Emulator)
    ETB buffer size: 2-8 KB
    XDS560v2 STM buffer size: 128 MB
Notes: 20

## Slide 21: System Trace
Pros
  Provides system level visibility to software thread execution and hardware performance
  CCS data visualization and analysis tools can process and display system trace data in a number of useful formats
  No additional hardware needed to use the ETB
Cons
  Only supported on select devices with an ETB or targets (device and board) that can support XDS560v2 Pro Trace
  Limited window of visibility when using the ETB due to limited buffer size
  XDS560v2 STM Trace:
    Supported by a limited number of devices
    Additional pins on the board for trace data
Notes: 21

## Slide 22: System Trace – Trace Viewer

## Slide 23: Trace Features Per Emulator
23
Device family | Technology | Emulator needed | HW modification required? | JTAG header connector required | Performance
Core/ Instruction | ETB | Any | No | Any | Small buffer
 | External pins | XDS560v2 PRO Trace | Yes | TI 60-pin or MIPI 60-pin | Virtually unlimited buffer
System | ETB | Any | No | Any | Small buffer
 | External pins | XDS560v21 XDS560v2 PRO Trace | Optional | TI 14-pin (slowest)2 cTI 20-pin, TI 60-pin or MIPI 60-pin (fastest) | Virtually unlimited buffer
1 Except XDS560v2 LC Traveler from Spectrum Digital
2 14-pin STM is not supported in all devices
Notes: This table summarizes the Trace features available per emulator family, and the main advantages and disadvantages of each. Basically the XDS560v2 PRO Trace is able to perform any type of Trace, while XDS560v2 only lacks Core pin trace, and the others are only able to do Trace if the device has an ETB.

## Slide 24: Trace Features Per Device
24
Type of Trace | Technology | Device family
Core / Instruction | ETB | C64x+ (C645x, C647x, DM64x) C66x ARM9 (AM180x, OMAPL13x, DM3x, DM644x, DM646x) Cortex A (AM33x, AM35x, AM37x, AM38x, DM37x, DM81x, OMAP4/5)
 | External pins | C64x (C641x, C645x, C647x, DM64x) C66x
System | ETB | AM335x AM38x C66x DM81x OMAP4/5
 | External pins | AM335x C66x OMAP4/5
* Newer devices may not appear on this list
Notes: This other table shows the features available per device. In summary, all devices that have a C6400, C6600 or an ARM core have some type of Trace, although only the C6000 devices sport Core Trace with external pins. Also, all devices that have an ARM core also have ETB, which automatically allows performing Core Trace using ETB but only the most modern are also capable of performing System Trace.

## Slide 25: Instrumented

## Slide 26: Compiler Path Profiling
Compiler instrumented code coverage
Data Collection
  Data is collected using the compiler Path Profiling capability
  Path profiler will add additional instrumentation code to the application
Supported on:
  C6x only
Notes: 26

## Slide 27: Compiler Path Profiling
Pros
  Instrumentation code automatically handled by the compiler
  Collected data can be used for generating profiling and code coverage reports
  Integrated with CCS IDE
Cons
  Additional compile/run time and memory footprint overhead
  RTS library must be used
  Application must reach exit point
  Following applications will need additional tweaking to support writing of path profiling data
    Non-terminating
    No main()
    Custom boot/initialization routine
    No run-time initialization model selected in the linker options
  JTAG connection required for C I/O call to write the PDAT file to the host (CCS uses JTAG to communicate to the target)
Notes: 27

## Slide 28: Path Profiling – Generate Code Coverage
cl6x --gen_profile_info
app.out
Execute
pprofout.pdat
pdd6x
test.prf
  cl6x -use_profile_info=test.prf --onlycodecov
Build and link to create instrumented executable
RTS function writes pprofout.pdat via C I/O
Profile data decoder
Saves overhead on target
Generates code coverage data

## Slide 29: Path Profiling – Generate Code Coverage
cl6x --gen_profile_info
app.out
Execute
pprofout.pdat
pdd6x
test.prf
  cl6x -use_profile_info=test.prf --onlycodecov
Build and link to create instrumented executable
RTS function writes pprofout.pdat via C I/O
Profile data decoder
Saves overhead on target
Generates code coverage data
Handled by CCS CodeGen Code Coverage processer

## Slide 30: System Analyzer / UIA
Real-time tool for analyzing, visualizing and profiling the performance and behavior of your application running on single or multiple cores
Data Collection
  Data is collected via software instrumentation using the UIA (Unified Instrumentation Architecture) target packages and can be transported via Ethernet, JTAG (run-mode and stop-mode), STM or USB/UART to the host PC for analysis
Supported on:
  C64x, C64x+, C674x, C66x, ARM9, Cortex-M3/4, Cortex-A8, C28x, MSP430
Notes: 30

## Slide 31: System Analyzer / UIA
Pros
  Visibility at the system level for SoC devices
    Correlate data from multiple cores on a common time line
  OS aware instrumentation data
    Context aware function profiling
  ‘Out of the box’ support for SYS/BIOS
Cons
  Requires use of the UIA target package
    Must be ported to run on non-SYS/BIOS OS
  Non custom configurations can require a good deal of setup
  Learning curve for effectively using UIA
Notes: 31

## Slide 32: System Analyzer
32
Tooling for analysis and visibility of single and multi-core systems
Instrumentation from multiple cores correlated to a common timeline
Predefined events for application benchmarking, execution, profiling, statistics, context change, errors/warning/info, etc.
Command channel for configuration and control of logging
Extensible Framework for data/command transports, loggers, services, decoders, analysis
Multi-Core Analysis Features