## Slide 1
SN6507EVM
Test Conditions:
Vin=12V，523KHz，Rilim: 18.2kohm(assume output current is 1.6A) Without Snubber, and Output Filter Inductor

## Slide 2
Vin = 12V
Vo = 22.8V
No-Load
(No RDC)
Vin = 12V
Vo = 15.7V
Load = 0.2A
No RDC
Vin = 12V
Vo = 18.1V
No-Load
(RDC=51k Duty Control)
Vin = 12V/0.29A
Vo = 14.57V
Load = 0.2A
(RDC=51k Duty Control)
Peak=900mA
Peak=448mA
200mA
500mA
CH2:SW2_V
CH1:SW2_I
CH3:SW1_V
CH4:SW1_I
Probe Setting
Deadtime is different?
Peak current is different?

## Slide 3: Vin=12V，523KHz，Rilim=18.2kohm(1.6A)，Electronics Load = 0.2A Without Snubber and inductor filter
58無Duty _No Load_VO=22.8
59無Duty _Load=0.2A_VO=15.7
60Duty _No Load_VO=18.1V
61無Duty _Load=0.2A_VO=14.57V，Vin=12V 0.29A
CC01 15V 60mA
CC02 15V 80mA
RS485、CAN=80mA
RB168MM150TR
CH2:SW2_V
CH1:SW2_I
CH3:SW1_V
CH4:SW1_I
Vin = 12V
Vo = 15.8V
Load = Short circuit

## Slide 4: Questions:
58無Duty _No Load_VO=22.8
59無Duty _Load=0.2A_VO=15.7
60Duty _No Load_VO=18.1V
61無Duty _Load=0.2A_VO=14.57V，Vin=12V 0.29A
CC01 15V 60mA
CC02 15V 80mA
RS485、CAN=80mA
RB168MM150TR
Why is there a different on equation between DC and non-DC control mode?
2. On the page 2 waveform, we found the deadtime is difference between DC and non-DC mode. How come?
And also, the current is 2 times difference in between? Could you help to explain from energy’s point of view?
3. On the page 3 waveform, when output rail is shorted to ground, there’re always 4 PWM cycles shutting off
and then turn on With 4 PWM cycles. In the d/s, it says when short event is happened, PWM will be cycle-by-cycle
protection. Is this waveform behavior correct?

## Slide 5: Answers:
CC01 15V 60mA
CC02 15V 80mA
RS485、CAN=80mA
RB168MM150TR
Why is there a different on equation between DC and non-DC control mode?
For converter designs with wide-input range but no duty cycle control, the turns ratio needs to take the minimum input voltage into consideration. When Duty Cycle control is enabled, the requirement of turns-ratio doubles as duty cycle is halved from 48% to 25%.
Here is a general formula for the inductor current. We still don’t figure out why peak current doesn’t match
this formula from physics perspective as the waveform shown on the page 2. (448mA vs. 900mA)
2. In the formula (21), how device implement it?
3. The reason why customer would like to look into this current is because the
Current rating of the Schottky diode needs to be selected correctly when DC is enabled.

## Slide 6
RB168MM150TR
2. On the page 2 waveform, we found the deadtime is difference between DC and non-DC mode. How come?
And also, the current is 2 times difference in between? Could you help to explain from energy’s point of view?
The peak current is due to primary inductance of the transformer and the change in on-time duration.
Is this deadtime difference observed with same transformer?
Yes, it’s the same transformer (From DELTA)

## Slide 7
RB168MM150TR
3. On the page 3 waveform, when output rail is shorted to ground, there’re always 4 PWM cycles shutting off
and then turn on With 4 PWM cycles. In the d/s, it says when short event is happened, PWM will be cycle-by-cycle
protection. Is this waveform behavior correct?
This depends on type of short, hard short or soft short. In soft-short the converter goes into hiccup mode
on hitting the programmed OCP threshold, the driver will be shut-off for 100 ns (typical), and then retry driving.
If the OCP trips again, the cycle continues.
It could be a “ Hard short ” as it’s shorted by Electronics load.
Why there’re five pulses observed during short circuit?
It’s about 5MHz/pulse. And in between the pulses, there is a
100ns shut-off time.
Is this short-circuit behavior a hiccup mode or cycle by cycle?
Could you explain more details!