## Slide 1
Devices Specification Table
Parameters | LM75A | LM75B | LM75C (obso) | TMP75 | TMP75B | TMP75C | TMP175 | TMP275
Operating Voltage Range | 2.4V to 5.5V | 3.0V to 5.5V (-3 and -5 options) | 3.0V to 5.5V (-3 and -5 options) | 2.7V to 5.5V | 1.4V to 3.6V | 1.4V to 3.6V | 2.7V to 5.5V | 2.7V to 5.5V
Operating Temperature Range | -55°C to 125°C | -55°C to 125°C | -55°C to 125°C | -55°C to 125°C | -55°C to 125°C | -55°C to 125°C | -40°C to 125°C | -40°C to 125°C
Quiescent Current | I2C Inactive, 0.28mA (typ) SD, 4µA | I2C Inactive, 0.25mA (typ) SD, 4µA | I2C Inactive, 0.25mA (typ) SD, 4µA | I2C Inactive, 50µA (typ) | I2C Inactive, 45µA (typ) at default | I2C Inactive, 15µA (typ) | I2C Inactive, 50µA (typ) | I2C Inactive, 50µA (typ)
Bit Resolution | 9 | 9 | 9 | 9 to 12 | 12 | 12 | 9 to 12 | 9 to 12
Conversion Time | 300ms (typ), 300ms (max) | 300ms (typ), 300ms (max) | 300ms (typ), 300ms (max) | 9-Bit: 27.5ms 10-Bit: 55ms 11-Bit: 110ms 12-Bit: 220ms | 20ms (min), 27ms (typ), 35ms (max) | 20ms (min), 27ms (typ), 35ms (max) | 220ms (typ), 300ms (max) for 12-bit | 220ms (typ), 300ms (max) for 12-bit
Accuracy | -25°C to 100°C: ±2°C -55°C to 125°C: ±3°C | -25°C to 100°C: ±2°C -55°C to 125°C: ±3°C | -25°C to 100°C: ±2°C -55°C to 125°C: ±3°C | -25°C to 85°C: ±0.5°C, ±2°C -40°C to 125°C: ±1°C, ±3°C | -20°C to 85°C: ±0.5°C, ±2°C -55°C to 125°C: ±1°C, ±3°C | 0°C to 70°C: ±0.25°C, ±1°C -20°C to 85°C: ±0.5°C, ±2°C -55°C to 125°C: ±1°C, ±3°C | −25°C to +85°C: ±0.5°C, ±1.5°C −40°C to +125°C: ±1°C, ±2°C | –20°C to 100°C: ±0.0625°C (typ), ±0.5°C (max) for 3.3V 0°C to 100°C: ±0.0625°C (typ), ±0.75°C (max) for 3V to 3.6V –40°C to 125°C: ±0.0625°C (typ), ±1.0°C (max) for 3V to 3.6V 25°C to 100°C: ±0.2°C (typ), ±1.5°C (max) for 3.3V to 5.5V
Timeout | 75 – 325ms | 75 – 325ms | No | 54ms (typ) | Min: 38ms, Typ: 54ms, Max: 70ms | Min: 20ms, Typ: 22ms, Max: 29ms | Min: 25ms, Typ: 54ms, Max: 74ms | Min: 25ms, Typ: 54ms, Max: 74ms
Power Supply Range For Specifications | 2.7V to 5.5V guaranteed performance | -3 option only guaranteed at 3.0V; -5 option only guaranteed at 5V | -3 option only guaranteed at 3.0V; -5 option only guaranteed at 5V | 2.7V to 5.5V guaranteed performance | 1.4V to 3.6V guaranteed performance | 1.4V to 3.6V guaranteed performance | 2.7V to 5.5V guaranteed performance | 2.7V to 5.5V guaranteed performance
Absolute Max Voltage | 6.0V | 6.5V | 6.5V | 7.0V | 4.0V | 4.0V | 7.0V | 7.0V
UL Certification | Yes | Yes | Yes | No | No | No | No | No
Max Temp Readout | 127.5°C | 127.5°C | 125.0°C | 125°C | 125°C | 125°C | 125°C | 125°C
ESD HBM | 2500V | 2500V | 1500V | ±4000V | ±2000V | ±2000V | ±4000V | ±4000V
ESD MM | 250V | 250V | 100V | ±300V | N/A | N/A | ±300V | ±300V
ESD CDM | 1000V | N/A | N/A | ±1000V | ±1000V | ±1000V | ±1000V | ±1000V
Package | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8) | SOIC8, VSSOP8 (MSOP8)
Notes: 1

## Slide 2: Devices Pin Out
Pin Out | LM75A | LM75B | LM75C | TMP75 | TMP75B | TMP75C | TMP175 | TMP275
1 | SDA | SDA | SDA | SDA | SDA | SDA | SDA | SDA
2 | SCL | SCL | SCL | SCL | SCL | SCL | SCL | SCL
3 | O.S. | O.S. | O.S. | ALERT | ALRT | ALRT | ALRT | ALRT
4 | GND | GND | GND | GND | GND | GND | GND | GND
5 | A2 | A2 | A2 | A2 | A2 | A2 | A2 | A2
6 | A1 | A1 | A1 | A1 | A1 | A1 | A1 | A1
7 | A0 | A0 | A0 | A0 | A0 | A0 | A0 | A0
8 | +Vs | +Vs | +Vs | V+ | Vs | Vs | V+ | V+

## Slide 3: Register Maps
Registers Name | LM75A | LM75B | LM75C | TMP75 | TMP75B | TMP75C | TMP175 | TMP275
Temperature | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00
Configuration | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01
 | 0x02 | 0x02 | 0x02 | X | X | X | X | X
 | 0x03 | 0x03 | 0x03 | X | X | X | X | X
Product ID | 0x07 | X | X | X | X | X |  | 
 |  |  |  | 0x02 | 0x02 | 0x02 | 0x02 | 0x02
 |  |  |  | 0x03 | 0x03 | 0x03 | 0x03 | 0x03
One-shot |  |  |  | X | X | 0x04 |  | 
Registers Name | LM75A | LM75B | LM75C | TMP75 | TMP75B | TMP75C | TMP175 | TMP275
Temperature | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00
Configuration | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01 | 0x01
 | 0x02 | 0x02 | 0x02 | X | X | X | X | X
 | 0x03 | 0x03 | 0x03 | X | X | X | X | X
Product ID | 0x07 | X | X | X | X | X |  | 
 |  |  |  | 0x02 | 0x02 | 0x02 | 0x02 | 0x02
 |  |  |  | 0x03 | 0x03 | 0x03 | 0x03 | 0x03
One-shot |  |  |  | X | X | 0x04 |  | 

## Slide 4: Configuration Register
Configuration Register | D7 | D6 | D5 | D4 | D3 |  | D2 | D1 | D0
LM75A | 0 | 0 | 0 | Fault Queue |  |  | OS Polarity | CMP/INT | Shutdown
LM75B | 0 | 0 | 0 | Fault Queue |  |  | OS Polarity | CMP/INT | Shutdown
LM75C | 0 | 0 | 0 | Fault Queue |  |  | OS Polarity | CMP/INT | Shutdown
TMP75 | OS | R1 | R0 | F1 |  | F0 | POL | TM | SD
TMP175 | OS | R1 | R0 | F1 |  | F0 | POL | TM | SD
TMP275 | OS | R1 | R0 | F1 |  | F0 | POL | TM | SD
TMP75B | OS | CR |  | FQ |  |  | POL | TM | SD
TMP75C | RSVD | RSVD | OS | FQ |  |  | POL | TM | SD

## Slide 5: Register
TMPs has and , but similar behavior and functionality.
Register | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
LM75A | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
LM75B | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
LM75C | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
TMP75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP175 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP275 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
LM75A | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
LM75B | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
LM75C | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | X | X | X | X | X | X | X
TMP75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP175 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP275 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: Register
Register | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
LM75A | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
LM75B | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
LM75C | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
TMP75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP175 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP275 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
LM75A | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
LM75B | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
LM75C | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | X | X | X | X | X | X | X
TMP75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP175 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP275 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMP75C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMPs has and , but similar behavior and functionality.