## Slide 1: Changan ethernet link down issue
Issue1: Mass production stage, only happened in power up, once link down it will always down, can’t self recovery, hard to reproduce
Issue2: Zongmu ECU 720(Mater) can detect link down, but front camera ECU 720(Slave) can’t detect
Front camera ECU – Tier1 Continental
TDA4
DRA821
DP83TG720
DP83TG720
DP83TG720
SOC
J3
SGMII
SGMII
Master
Master
SGMII ?
ADAS ECU – Tier1 Zongmu
MDI

## Slide 2: Debug proposal
Dump failure mode 720 registers(from 0x0 ~0x60a) both ADAS ECU and Front camera ECU - Zongmu+ Conti
Probe failure mode 720 LED0 pin to double check whether link down both ADAS ECU and front camera ECU - Zongmu+ Conti
Check power sequence of 720 whether meet our requirement - Zongmu+ Conti
Check crystal circuit test report(from crystal vender) - Zongmu+ Conti
Check software configuration whether using our SNLA371 file section 3 guideline - Zongmu+ Conti