## Slide 1: ESD2CAN24-Q1 | Technical Competitive Comparison Matches or beats existing solutions specs!
Devices | ESD2CAN24-Q1 | PESD1CAN | SZNUP2105 | SESDONCAN1 | SZMMBZ27VCLT1G
Working Voltage (VRWM) | ±24V |  |  |  | 22V
16A TLP Clamping Voltage Indicates how well solution protects from 8kV ESD strike Learn More: Video ¦ Article | 33V | ~47V (est) | ~40V (est) | ~44V (est) | 38V
Capacitance Impacts System Bandwidth ¦Learn More: Video ¦ Article | 3.2pF | 17pF | 30pF | 10pF | N/A
IEC 61000-4-2 (ESD) System Level ESD Immunity Standard Learn More: Video ¦ Article | 30kV | 23 kV | 30kV | 23kV | 30kV
ISO 10605 (ESD) 330 pF / 330 Ohms Automotive System Level ESD Immunity Standard Learn More: Article | 30kV | 20 kV | Not Available | Not Available | N/A
Max Leakage ( IRM ) | 50nA | 50nA | 100nA | 100nA | 100nA
Auto (Q101) Qualified |  |  |  |  | 
Status | New | NRND (Not Recommended for New Designs) | Active | Active | Active
Packages | SOT-23, SC-70 | SOT-23 | SOT-23 | SOT-23 | SOT-23