## Slide 1: GTK schematic review

## Slide 2: TUSB8041 Hub2 review
1: if there is no AC cap on hub 1 downstream port, C8113/C8114 should be 100nf.

## Slide 3: TUSB8041 hub2 review
1: Test pin should be grounded
2: Power switching and overcurrent is not implemented

## Slide 4: TUSB8041 hub2 review
1: USB_vbus0, USB_vbus1 are for Device0-Device1 VBUS? What is max current for USB_vbus0, USB_vbus1