## Slide 1: Link training limitation with limited redriver
Link 2
Link 1
Link Training: Aux Channel negotiates source TX VOD, Pre-emphasis and link data rate so that sink can receive main link data with acceptable error rate
In Aux snooping mode, there could be inter-op issues because the link training configuration being requested by the receiver is based upon the signal path between the limited redriver and the receiver(Link 2 as shown above) not the actual signal chain(Link 1). Problem gets worse with long cable and if there are multiple redrivers w/ the same aux snooping scheme placed in series as shown above
The scalar would request pre-emphasis and voltage swing level based upon the output of the redriver2 (Link 2). Redriver1 and Redriver2 would adjust its EQ, pre-emphasis and voltage swing accordingly based upon the request from the scalar. DP Source also outputs data based upon the request received from the scalar. Many link training errors and even if link training passes, bad SI(jitter can also be amplified) will be created by using Aux Snooping