## Slide 1: Background
Defect
  team found system failed to display correct DIMM inventory data in BMC web. DIMM 1-8 are always loss.
  Glitchy waveform was found during time frame of BMC trying to communicate with group of DIMM 1-8.
Glitch happened on I2C low

## Slide 2: Topology is different between MB pass2 & pass3
Commonality block revised to move I3C level shifter (TCA39416) out of block to save cost
MB is brand new topology because TCA39416 is moved to before mux. Location of TCA39416 is different from verified pass 2 design.
10.9”
MUX
13”
0.3”
TCA39416
3.8” – 6.5”
MUX
BMC
TCA39416
MUX
13.5”
TCA39416
MUX
BMC
1.8”
TCA39416
0.12”
MUX
TCA39416
2” – 5.5”
0.2”
2.9”
1.1”
2.9”
1.1”
CONN
CONN
11”
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM 9-16
DIMM 1-8
3.8” – 6.5”
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM 1-8
1.85”
1.8”
MUX
2” – 5.5”
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM 9-16
TCA39416 been moved out of commonality block
Pass 2 Topology
Pass 3 Topology
1.0V domain
1.8V domain

## Slide 3: Accelerating circuit inside TCA39416 causes glitch
Reflection may trigger accelerating from TCA39416. That causes unexpected glitch.
BMC
DIMM
DIMM
DIMM
VGS=1V
VDS < 1V
VDS < VGS-VTH
Triode mode >> TCA39416 acts like damping (Rds-on) in analog topology.
Not an end point, may receive reflection!

## Slide 4: Electrical Perspective
BMC
VGS=1.8V
VDS ~ 0.8V
VGS < Vth, FET inside TCA39416 cutoff
Not an end point, may receive reflection!
1.0V
1.8V
1.8V
1.0V
To muxing circuit
BMC
VGS=1.8V
VDS = 1V
VDS > VGS-VTH
Saturation mode
1.0V
1.8V
1.8V
1.0V
To muxing circuit
BMC
VGS=1.8V
VDS << 1V (below VGS-Vth)
VDS < VGS-VTH
Triode mode >> TCA39416 acts like damping (Rds-on) in analog topology.
1.0V
1.8V
1.8V
1.0V
To muxing circuit
High
1.0V
1.8V
High to low
High to low
VGS=0V
VGS=1V
Low
Low
VGS=1V
Reflection
BMC
VGS=1.8V
1.0V
1.8V
1.8V
1.0V
To muxing circuit
VGS=1V
Low
Reflection
TCA39416 A side senses reflection as a low to high edge transition. B side pull up bypass asserted
BMC
VGS=1.8V
1.0V
1.8V
1.8V
1.0V
To muxing circuit
1.0V
1.8V
VGS=0V
High to low
Low
B side achieved logic high, pull up bypassing de-asserted. Voltage been pulled back to low by BMC
High to low
VDS = 1V
1. XCC logic high, keep high by pulled resistor
2. XCC start pull signal to low
3. XCC pull low to low, FET enter triode mode act like damping in middle of signal path. Reflection might happen
4. TCA39416 sensed reflection and treat it as low to high edge transition. Pull up resistor bypassing asserted. Pull voltage to high
5. TCA39416 de-assert pull up bypassing after voltage reach to high. Voltage been pulled to low

## Slide 5: Cannot completely eliminate glitch with only tuning BOM items
Adjust damping resistors nearby DIMM
Remove extra pull up resistor
Adjust damping resistors on SCM
Adjust damping resistors nearby mux (branch of DIMM 1-8)
Bypass mux by jump wire
Adjust DIMM population condition (0 DIMM, 1 DIMM, full DIMM…)
Best improve (still glitch)
Default (full glitch)

## Slide 6: Bypass TCA39416
Both function-wise and signal-wise got fixed.
All DIMM display in XCC inventory
Signal is glitch-free