## Slide 1: TCAN1043 vs TCAN1043A
ASC-INT-TRX
September 9, 2021

## Slide 2: Migrating from TCAN1043 to TCAN1043A (Key Specs)
Parameter | TCAN1043(H) |  | TCAN1043A
CAN Data rate | CAN FD upto 2 or 5 Mbps |  | CAN FD upto 8 Mbps
CAN Bus Fault | ±58 V (±70 V) |  | ±58 V
RX Common mode | ±30 V , ±12 V in sleep |  | ±12 V
VSUP Abs Max | 58 V (70 V) |  | 45 V
VSUP Op Range | 4.5 – 45 V (60 V) |  | 4.5 – 40 V
VSUP UV | 3 V – 4.2 V |  | 3.5 – 4.25 V (Falling) 3.85 – 4.4 V (Rising)
Operating TJ | -55 to 150 °C |  | -40 to 150 °C
VIO Range | 2.8 – 5.5 V |  | 1.7V – 5.5 V
VIO UV | 1.3 V – 2.75 V |  | Falling: 1 V (min) Rising: 1.65 V (max)
INH Output | High Z when output disabled |  | 4MΩ pull-down on INH when disabled ( sleep mode )
Logic Pins Abs Max | 7 V |  | 6 V
IIH at EN and nSTB | 10 µA |  | 115 µA (due to lower value of pull-down resistor)
Migrate to TCAN1043A-Q1 easily
Pin to Pin compatibility
Differences highlighted – all other parameters remain unchanged
Small SOT package (DYY) for space-saving applications
Pin-to-Pin Drop-in
SOIC: 8.65 x 3. 9 mm
SOT: 4.2 x 2 mm New
VSON: 4.5 x 3 mm

## Slide 3: Migrating from TCAN1043 to TCAN1043A (Details)
Section | TCAN1043(H) | TCAN1043A
CAN Bus Biasing | Fixed Bus Biasing (2.5 V in Normal, GND in STB/Sleep) | Autonomous
Mode Behavior | CAN transmitter would transmit dominant until the TXDDTO timer expired | CAN driver disabled if TXD=0 when entering CAN Bias Active (TXDCLP)
 | UVIO, UVCC always run the 300ms Sleep timer (TUV). VIO and VCC need to be above the UV thresholds within TUV after powering up or after entering Standby mode from Sleep mode due to Wake event. | UVIO, UVCC 300ms Sleep timer (TUV) is disabled until VIO/VCC are good. Allows for indefinite power up time. Sleep Wake Error (SWE) timer transitions the device into Sleep mode after 4 minutes (tINACTIVE) if the device is stranded in Standby mode due to (a) VCC/VIO not powering up properly or (b) MCU fails to transition the device into Normal mode.
 | VCC Supervisor ON in Sleep mode – VCC > UVCC automatically transitions the device into normal or silent mode | VCC Supervisor Off in Sleep mode – Explicit toggling of nSTB from low-to-high required for transition into normal/silent mode (e.g. if the device enters sleep mode due to UVCC).
 |  | VIO < UVIO transitions the device from normal to Standby mode
 | NFAULT pin is driven high during sleep mode (if VIO is present) | NFAULT pin is high-Z in sleep mode (even if VIO is present)
3
Migrate to TCAN1043A-Q1 easily
Pin to Pin compatibility
Differenced highlighted – all other parameters remain unchanged
Small SOT package (DYY) for space-saving applications
SOIC: 9.9 x 3.91 mm
SOT: 4.2 x 2 mm
VSON: 4.5 x 3 mm

## Slide 4: Thermal Table
THERMAL METRIC |  | TCAN1043x-Q1 |  | TCAN1043A-Q1 |  | UNIT
 |  | D (SOIC) | DMT (VSON) | D (SOIC) | DMT (VSON) | 
RθJA | Junction-to-ambient thermal resistance | 78 | 33.1 | 87.1 | 39.7 | °C/W
RθJC(top) | Junction-to-case (top) thermal resistance | 33.6 | 30.5 | 41.8 | 41.1 | °C/W
RθJB | Junction-to-board thermal resistance | 34.7 | 10.8 | 43.7 | 15.9 | °C/W
ΨJT | Junction-to-top characterization parameter | 5.7 | 0.4 | 8.5 | 0.9 | °C/W
ΨJB | Junction-to-board characterization parameter | 34.3 | 10.7 | 43.3 | 15.9 | °C/W
RθJC(bot) | Junction-to-case (bottom) thermal resistance | n/a | 1.3 | N/A | 6.6 | °C/W