## Slide 1: TPS65986 issue

## Slide 2: TPS65986 issue
PC
Mother board
DP source
connector
USB3.0
connector
Luxshare TPS65986
DP Adapter
DP Pad
USB Pad
C
Monitor
C
Type-C cable
System overview:
r
PC chassis
Picture 1: System overview

## Slide 3: TPS65986 issue
Real system overview:
DP and USB
Adapter
PC Mother board
Picture 2: Real system

## Slide 4: TPS65986 issue
Normal operation:
In normal operation, the monitor is using to display the DP signal.
Abnormal operation (issue):
Customer unplug the type-C cable and Plug it again, sometimes the monitor can not display(black screen).
Analysis for Normal operation:
Using the CC logic equipment to monitor the CC log, we found that in normal operation, the customer adapter is DFP, and the monitor is in UFP(DPF have 1 PDO to UFP). In this way, the monitor can enter ALT mode success, and the monitor can display success.(pls see page 5 for the Picture 3: normal cc log or check “M625Q_A9 CPU+P27U Normal.ccgx” in the email attachment)
Analysis for Abnormal operation:
Using the CC logic equipment to monitor the CC log, we found that in abnormal operation, the customer adapter is UFP, and the monitor is in DFP(DPF have 4 PDO to UFP).
In this way, the customer adapter(TPS65986 inside) didn’t enter PR_Swap or DR_Swap, and the communications stops. So it’s failure to enter the ALT mode.(pls see page 6 for the Picture 4: abnormal cc log or check “M625Q_A9 CPU+P27U abnormal.ccgx” in the email attachment)

## Slide 5: TPS65986 issue
Picture 3: normal cc log

## Slide 6: TPS65986 issue
Picture 4: abnormal cc log

## Slide 7: TPS65986 issue
Question:
1,When the monitor in DFP, it seems the communication is stop so cause the failure. How to trigger PR_Swap or DR_Swap for normal operation?
2, Customer using the “TUSB546EVMFlash.bin” for the Flash program memory（check the bin file in attachment) ,
in order to fix the questions, pls help to updated the attachment TUSB546EVMFlash.bin for the external Flash memory configure file.