## Slide 1: TUSB8020 Schematic review

## Slide 2: TUSB8020 review
1: remove R274 on GRSTz

## Slide 3: TUSB8020 review
1: remove R147 on SMBUSz if you don’t plan to change configuration with SMBUS

## Slide 4: TUSB8020 review
Change to it’s full name on pin 35/36

## Slide 5: TUSB8020 review
For TUSb8020B, 1 is active low for PWRCTL_POL, if you pullup, means active low for PWRCTL ,but TPS2561 is EN high to enable the switch

## Slide 6: TUSB8020 review
If PWRCTL_BATEN is pulled up, it mean battery charging is enabled, is this what you want?