## Slide 1: Texas Instruments High Speed Amplifiers Simple Transimpedance Designs Using High Speed Op Amps
November, 2014
Michael Steffes/Xavier Ramus

## Slide 2: Agenda
Basic Issues
Detailed Design equations
Examples of Simple Design
Advanced Transimpedance Designs
Measuring Frequency response for Capacitive source circuits
Detecting and amplifying the often very small current signal coming from a photodiode, can present a considerable challenge. The achievable gain, bandwidth, and input referred noise current are all coupled together in a few design variables.
Most of this material comes from a series of articles referenced at the end where that material is also summarized in TI application note SBOA122.
Many of the slides include more detail in the notes pages.

## Slide 3: Design Issues Covered
Op Amp based, high performance, transimpedance designs can be analyzed using a single pole op-amp model to give a 2nd order closed loop transfer function. Although the full transfer function doesn’t suggest a design approach, some judicious simplifications will lead to a very simple, and accurate, amplifier compensation methodology.
A simple equivalent input noise current equation, correctly including all of the high frequency terms (but neglecting 1/f effects), will allow an easy comparison between design solutions for their achievable sensitivity
Notes: While dedicated transimpedance amplifiers exist for OC-x standards, a myriad of other applications can benefit from the design flexibility offered by a voltage feedback operational amplifier solution.
Quite a lot of earlier design discussions have suggested placing the feedback pole at the intersection of the rising noise gain and the open loop gain curve - this works but yields a slightly peaked response causing unnecessary pulse response overshoot and ringing.

## Slide 4: Transimpedance Design (cont.)
Numerous articles and discussion in the literature - several key misconceptions have complicated this application for many designers.
Unity gain stability in the op amp is not required - a lot of literature suggests that it is.
Feedback compensation is required even if a unity gain stable op amp is used.
Many applications have an output noise spectrum dominated by the effect of the input noise voltage (not current) gained up to the output by the differentiator formed by the diode capacitance at the inverting node and the feedback resistor - this is often neglected.
Putting the feedback pole at the intersection of the noise gain zero and the open loop gain curve is ideal? This is actually incorrect and yields a closed loop 2nd-order response with a Q ≈ 1 giving a step response that will overshoot and/or a frequency response that is peaking 1.25dB.

## Slide 5: Transimpedance Frequency Response Analysis Circuit
Deceptively simple looking circuit - that causes considerable difficulty in application. Cd is the diode capacitance plus wiring parasitic. Cs, used for design, is the total on the inverting node.
Notes: This circuit is complicated by the effect of Cd on the noise gain for the op amp. To get a correct solution for Cf to hit a target closed loop frequency response, include the differential input capacitance for the op amp and one common mode capacitance (that on the inverting node).

## Slide 6: Controlling the Frequency Response
Key variables required to determine Cf to get the desired frequency response
  Total Capacitance on the Inverting node
    Be careful to include the op amp input parasitic capacitance. Cd is the detector diode capacitance under the expected reverse bias plus wiring parasitic.
  Gain Bandwidth Product of the op amp
    The higher the gain bandwidth, the higher the resulting closed loop transimpedance bandwidth. In general, the op amp does NOT need to be unity gain stable. As will be shown, loop gain x-over typically occurs at a very high noise gain - so very wideband, non-unity gain stable, op amps can be used to get their lower input voltage noise.
  Desired transimpedance gain or bandwidth
These are interrelated - for a particular op amp selected, targeting the gain will set the maximum bandwidth or, conversely, targeting the bandwidth will set the maximum gain.

## Slide 7: Full Laplace Transfer Function for the Transimpedance Op Amp Configuration
Transimpedance Gain
Where:
Single pole, open loop gain model
Gain Bandwidth Product (GBP)
Notes: Although we are normally very interested in the higher frequency open loop
poles for the op amp, they can be ignored in this analysis to greatly
simplify the results.
Using just a dominant single pole open loop gain model for the op amp,
and developing the closed loop transfer function from Id to Vo for the
transimpedance configuration, gives a relatively complicated looking
2nd order transfer function.
It is a valid approximation to ignore the higher order poles since we will be
dropping to unity loop gain at a relatively low frequency due to the noise
gaio shaping experienced in this circuit.

## Slide 8: Standard ωO and Q form for this 2nd-Order Transfer Function.
Notes: Manipulating this full transfer function into a filter analysis format - gives the Wo and Q shown above.
If we have picked an amplifier, the Gain Bandwidth Product is set.
If we have picked a diode, the inverting node capacitance is set.
We are then left with just Rf and Cf to control both Wo and Q. Should be able to arrive at a solution.

## Slide 9: Loop Gain Analysis
It is often instructive to look at the op amp circuit in loop gain form to view what each of the critical elements in the design mean graphically.
The loop gain plot shows the open loop characteristic of the op amp with the noise gain superimposed - that gain starts out at 1 (0dB) then rises at Z1 with single zero response caused by the feedback resistor and inverting input capacitance (Cs) up to the pole formed by Rf and Cf. Several important points to note -
  FO is in fact the characteristic frequency of the closed loop response.
  Noise gain at x-over is 1+Cs/Cf which can be very high - hence, unity gain stability in the op am is not required.

## Slide 10: Bode Plot of the Loop Gain for the Transimpedance Op Amp Configuration
Gain Bandwidth Product (GBP)
Log Frequency (Hz)

## Slide 11: Analysis Simplifications
Algebraic simplifications to get an easy compensation solution.
  With Cs >> Cf, drop Cf from Z1 Equation
  Let (AOL + 1).wa/2 = GBP (gain bandwidth product in Hz)
    This is simply neglecting the “1”
  Drop the “1” in (1 + Aol(Cf/(Cs+Cf))
Notes: An exact solution for Cf to get a target Q is extremely complicated - it can be considerably simplified by ignoring a few terms with a very minor error in the resulting value for Cf.

## Slide 12: Simplified Expressions for Fo and Q
The 2nd-order characteristic frequency is fixed by
the Amplifier Gain Bandwidth Product
and the zero formed by the transimpedance gain resistor and the source capacitance
The Q of the 2nd-order closed-loop transfer-function is simply the
ratio of the pole frequency set in the feedback path to the
characteristic frequency (P1/FO) which is also equal to the ratio of
the characteristic frequency to the intersection of the open loop response.
with the high frequency noise gain (1+Cs/Cf) - this is FO/Fc.
Notes: These two equations give a very simple path to transimpedance design.

## Slide 13: Design Methodology
The next slide steps through finding the maximum available transimpedance gain for a given op amp and diode if a maximally flat Butterworth response is the target design. This target is interesting in that if we set P1 at 0.707*FO, it circles back to give us a F-3dB equal to FO. Kind of unique and interesting design point.
More general targets with peaking can be designed using the initial equations.
A very useful alternative way to use these equations is to know your desired transimpedance gain and bandwidth and use them to solve for the minimum required GBP. Then the compensation capacitor (Cf) can be calculated using an amplifier with a GBP > than that minimum, along with this target transimpedance gain. The calculation for Cf is shown on the next slide.

## Slide 14: Design Simplifications
If a target of Q = 0.707 is set, a very simple design methodology results.
At Q = 0.707, the 2nd-order closed-loop response gives an F-3dB = FO
So, if we set P1 = 0.707*FO, we get an F-3dB = FO
Assuming this - and then targeting an F-3dB, sets the FO target in a design.
Maximum achievable gain given
,
,
and target
(With Q = 0.707)
Notes: This slide steps through finding the maximum available transimpedance gain for a given op amp and diode if a maximally flat Butterworth response is the target design. This target is interesting in that if we set P1 at 0.707*Fo, it circles back to give us a F-3dB equal to Fo. Kind of unique and interesting design point.
More general targets with peaking can be design using the initial equations.
A very useful alternative way to use these equations is to know your desired transimpedance gain and bandwidth and use them to solve for the minimum required GBP. Then using an amplifier with a GBP > than that minimum, along with this target transimpedance gain, can be designed using the Cf calculation on the next slide.

## Slide 15: Simplified Design Continued
  With maximum achievable gain (RF) set, can go back and set Cf to put P1 where it needs to be for Q = 0.707
Notes: Using the F-3dB from the previous slide (which, with the Q=.707 constraint, occurs at the geometric mean of the GBP and the zero in the noise gain) and this maximum Rf, Cf can be solved
Lower Rf’s if needed by the design can be used and placed into this equation as well.

## Slide 16: Total Equivalent Input Current Noise Calculation
The total input referred current noise equation that often appears in the High Speed Amplifier group de-compensated voltage feedback op amps uses several simplifying assumptions to arrive an approximate expression. Specifically -
  This is an integrated noise analysis that uses spot noise over frequency - not intended as a spot noise equation for narrowband applications.
  We are assuming the application is DC-coupled, pulse oriented where the integrated noise is of interest.
  The final signal bandwidth for both the transimpedance design and any post-filtering is >10X the 1/f noise corner for any of the op amp noise terms - this allows those effects to be neglected for integrated noise purposes
  While the amplifier must be compensated with a feedback capacitor, it is much simpler for noise calculation purposes to assume a noise power bandwidth lower than this that will be set further downstream in the signal path. This means the target transimpedance bandwidth should be set > than the bandwidth that will be set by post-filtering.

## Slide 17: Total Input-Referred Equivalent Input-Noise Current for Wideband Transimpedance Design

## Slide 18: Simplified Transimpedance Noise Analysis
A thorough expression for transimpedance output noise can be extremely complicated This principally arises from two issues –
Including 1/f effects in the analysis - neglecting those for broadband applications creates a slight error but considerable simplicity.
Allowing each noise term to be combined at the output with a frequency response set only by the transimpedance amplifier design itself. If we assume the transimpedance stage is designed to provide > than the desired final signal bandwidth, a post-filter downstream can be assumed for noise power bandwidth limiting purposes. That frequency “F” can then be used to calculate integrated noise.

## Slide 19: Input Noise Terms
The input noise terms needed for a transimpedance design are shown on the next slide. These include –
Non-inverting input voltage noise (en - this will have a gain to the output of “1” at DC then increasing at 20dB/decade beyond (1/2RfCs)Hz which is the zero frequency (Z1) in the noise gain.
Inverting input current noise (ibi) –
Feedback resistor noise voltage = (4kTRf)
These last two terms will, strictly speaking, have a response pole to the output set by P1. Since we will be assuming a post-filter below P1, we will neglect this internal band-limit and just apply an integration frequency of “F” to all the noise terms.

## Slide 20: Transimpedance Noise Analysis Circuit
+
-
Voltage Feedback
Op Amp
Notes: The input noise terms needed for a transimpedance design are shown here. This includes -
1. Non-inverting input voltage noise (en - this will have a gain to the output of “1” at DC then increasing at 20dB/dec. beyond (1/2RfCd)Hz which is the zero frequency (Z1) in the noise gain.
2. Inverting input current noise (ib)
3. Feedback resistor noise voltage = (4kTRf)
These are all shown as spot noise voltage and current density terms - they can be combined at the output times their gain then squared to get power. No feedback cap. is shown for this analysis but is absolutely required for stability.

## Slide 21: Gain for the Noise Terms to the Output
The resistor voltage noise shows up directly at the output with no gain. Square that to get noise power
The amplifier’s inverting input current noise shows up at the output times the feedback resistor. Square that to get the noise power
The amplifier’s input voltage noise has a gain to the output that traces out the noise gain curve shown earlier in the Bode analysis. Only the zero is considered here since we will assume a frequency of integration that is less than the pole and set by a post-filter. Again, square this output noise voltage term to get power.

## Slide 22: Total output noise power
To get the total output noise power, take each noise term times its gain to the output, square it, then add.
Note that this circuit does not show a feedback capacitor - that capacitor (Cf) is absolutely required for stability but is not shown here since the noise integration frequency is assumed to be less than the pole set by (1/2RfCf)Hz = P1

## Slide 23: Input-Referred Equivalent Input Noise Current
Input refer eo2 by dividing by
Frequency dependent term
Notes: To compare different designs, it is more common to compare equivalent input referred current noise. We are essentially trying to develop an equivalent input noise current value that is flat over frequency that will integrate to the same output noise power over the “F” noise power bandwidth as the actual amplifier output noise would.

## Slide 24: Getting an average value for the last term.
The final term in the total input-referred noise-current expression increases with frequency - this is the differentiated input noise voltage of the op amp that will appear at the output. To get an average equivalent value, this must be integrated over F then divided by F. Strictly speaking, a starting integration value of 0Hz is not physically correct - but can be used as a simplification.
For f = 0 F
Average the noise power
of the 4th term over the noise power bandwidth - “F”

## Slide 25: Input Referred equivalent input noise current
This average value over “F” for the last term may now be combined with the other 3 terms that have no frequency dependence to get the total equivalent input referred current noise expression.
This input referred spot noise current will integrate to the same total output noise power as the actual output noise spectrum if the frequency span of integration is limited to “F”. This expression is what shows up in the data sheets.

## Slide 26: Equivalent Input Spot Current Noise for Output Noise Integrated to F < P1

## Slide 27: Design Examples - Getting a Target Bandwidth Given a Source Capacitance
  Select an Op Amp with a particular GBP - include its input parasitic capacitance + the source diode capacitance to solve for Z1 given the desired bandwidth and actual GBP. With Z1 set, solve for achievable maximum gain, = Rf to get the minimum input referred noise current.
  2. Set P1 at Q * FO. Use this and Rf to solve for Cf.
  3. Check that 1 + Cs/Cf > minimum stable gain for the op amp selected

## Slide 28: Wideband VFB Op Amps Suitable for Transimpedance design

## Slide 29: Example Design #1, 20Mhz from 20pF
In this case we are starting with a source capacitance a target bandwidth and
an amplifier and seeing how high a transimpedance gain we can get, then we
compute the input-referred noise, integrating through P1.

## Slide 30: Example Design Using a Wideband Bipolar Input Op Amp.

## Slide 31: Example Design #2, 2Mhz from 200pF
In this case we are starting with a source capacitance a target bandwidth and
an amplifier and seeing how high a transimpedance gain we can get then
computing the input-referred noise, integrating through P1. Here we select a JFET device as the Rf will be too high for a bipolar input bias current

## Slide 32: Example Design Using a Wideband JFET Input Op Amp

## Slide 33: Design Discussion
The OPA657 design yielded 5pA equivalent input noise current if we assume a noise power bandwidth limit set to 1.4Mhz. This is totally dominated by the 3rd-term of the total noise equation – the effect of the rising portion of the noise gain curve times the relatively high 4.8nV input voltage noise for the OPA657.
Repeating this design using the OPA846, with its much lower voltage noise but much higher current noise, actually yielding a lower equivalent input noise current. – Specifically, the OPA846 will give the same bandwidth and an input noise of 3pA vs. 5pA for the OPA657.
So why don’t we use the OPA846??

## Slide 34: High Gain Design Repeated with the OPA846

## Slide 35: OPA846 Options at 310kΩ
If we look at the effect of the OPA846’s 19mA input bias current using a 310kW feedback, we would see a 5.89V output-offset voltage.
Adding a 310kW resistor on the non-inverting input will allow bias current cancellation, but will now put a 5.89V common mode voltage on the inputs – which is out-of-range for a +/-5V operation.
There is a way around this -
The T-feedback structure has the interesting effect of also reducing the required input-matching resistor to get bias-current cancellation. This can be used to bring the input common mode voltage into range.
Whenever this bias current cancellation is used for a transimpedance design, it is imperative to decouple that resistor to kill its noise contribution.

## Slide 36: Adapting a Transimpedance Design to the T-Feedback structure
Essentially, we implement an equivalent feedback impedance with an initial resistor out of the summing junction towards the output then implement a voltage divider that will have the effect of gaining up that impedance.
From an initial single resistor design, decide how much voltage divider gain you want, divide the original resistor by that value and multiply the compensation capacitor by that value.
The 310kΩ design is adapted to the OPA846 by using a gain of 10V/V resistor divider – this will reduce the required bias current cancellation resistor to 31kΩ significantly reducing the common-mode voltage generated by the input bias current.
That new circuit is shown on the next slide.

## Slide 37: High Gain Design Repeated with the OPA846 Modified to the T-network in the feedback
This approach does work, but will have much higher output-offset voltage than the OPA657.

## Slide 38: Modified OPA846 Transimpedance Frequency Response
This also simulated out to approximately 3pA input-referred current-noise if F = 1.4MHz

## Slide 39: Increasing Performance of a Transimpedance Design.
If the required design does not reach the needed gain or bandwidth for a given detector capacitance, one way to improve performance without impacting noise too much is to use an imbedded gain stage.
Adding a wideband gain stage inside the loop increases the gain-bandwidth product directly. This allows either the bandwidth for a targeted gain to be increased or the gain for a targeted bandwidth to be increased at a square-root rate.
For instance, adding a gain of 4 inside the loop will give the option of either a doubled gain or bandwidth.

## Slide 40: Embedded Gain Transimpedance Design
Use Av *GBP to work through this design.

## Slide 41: Using a Network Analyzer to Test a Transimpedance Amplifier Design
Often, the actual diode and its response is not well known. It is very useful to be able to separately test the AC performance of a proposed design.
This can be done using a network analyzer where it feeds first into a 50ohm series resistor and then into a capacitive divider.
At higher frequencies, the capacitors short out and the network analyzer see its desired 50ohm termination.
The caps. Act like a current divider sending a small portion of the current through the series 50ohm into the series cap that connects to the circuit under test.
The apparent source impedance looking back into the circuit becomes the series capacitor at high frequency

## Slide 42: Using a Network Analyzer to Test a Transimpedance Amplifier Design

## Slide 43: Added Transimpedance Design Resources
1.“Control Frequency Response and Noise in Broadband, Photo detector Transimpedance Amplifiers” Michael Steffes
  EDN, Design Feature - July 4th, 1996 pp113-125
2.”Embedded gain supercharges FET- transimpedance amplifier”. Michael Steffes
  EDN, Design Feature – May 22nd, 1997 pp129-142
3. “Here’s an Easy Way to Test Wideband Transimpedance Amplifiers”. Michael Steffes
  Electronic Design, Analog Application Issue - June 8th, 1998 pp74-80
“Transimpedance Considerations for High-Speed Operational Amplifiers”. Xavier Ramus
  http://focus.ti.com/general/docs/litabsmultiplefilelist.tsp?literatureNumber=sboa122
High Speed Amplifiers offering from Texas Instruments that include a transimpedance design discussion and greater than 1.5GHz GBP.
    OPA657, JFET Input, 1600MHz Gain Bandwidth
    OPA846, Gain of 7 stable, 1750MHz Gain Bandwidth
    OPA2846 dual, gain of 7 stable, 1750 MHz GBP
    OPA847, Gain of 12 stable, 3900MHz Gain Bandwidth

## Slide 44: Conclusions for Transimpedance Compensation and Noise Analysis
The closed loop response is a 2nd order low pass, where:
  The characteristic frequency is always the geometric mean of the zero in the noise gain and the op amp’s gain bandwidth product.
  Placing the feedback pole only changes the Q of the response. Setting P1 = 0.707 * FO will give a closed loop Butterworth response with F-3dB = FO
Since the noise gain always crosses over the open loop gain at a high value if compensated correctly, the op amp does not need to be unity gain stable.
The output noise can be strongly influenced by the peaked up voltage noise term.
Generally, Bipolar Inputs are better for low to moderate gains at wider bandwidths while JFET inputs are better for high transimpedance gains at lower bandwidths.
With Bipolar inputs, a resistor equal to Rf is placed to ground on the non-inverting input to improve DC accuracy - this must be bypassed with a capacitor to kill its noise contribution.
If high Rf are needed on a bipolar solution, consider the T-network approach to keep the common mode voltages in range.