## Slide 1: PRAMPS in PIR Motion Sensing Summary of Implementations and Needs
Passive / Pyroelectric infrared
Sensor BW: 10 Hz
Gain needed: ≥500V/V
Slow to start up  always on
3 Implementations
AFE: Dual op amp & window comparator
Mixed: Dual op amp and ADC (in micro)
Digital: Digital PIR sensor module
Key Op Amp Parameters
Wireless & Bus
GBW
  >5 kHz
IQ
  Lower is better
    Wireless systems use batteries  longer battery life
  Bus-powered  more nodes per bus / hub
Wired
Cost
Package
Most op amps have the same pinout  customer preference leads / no-leads
Hero Products:
  OPA/TLV2369
  TLV8812
10 Hz BW
AFE Implementation
1. PIR Sensor
2. Filtering &
Amplification
3. Threshold
Detection

## Slide 2: PRAMPS in Smoke and Heat Detector
Battery life longevity (low power)
Accurate measurement (low Vos)
I-V conversion (low Ib)
Very low power, precision CMOS
Hero products: LPV821, LPV812, OPA369
Broad low power product offerings
Wide selection of micro and nano power amplifiers
Requirements
Solution
TI Value
EE | Type | Key specs | GPN’s
Smoke detector | With ionization | Very low power Low offset voltage Low drift | LPV821 LPV811 LPV812
Smoke detector | with thermistor | Very low power Low offset voltage | OPA369, TLV369 LPV811, LPV812
CO sensor (toxic gas) | Vref | Low power Low output impedance | OPA369, OPA348, TLV369
CO sensor (toxic gas) | Potentiostat | Low power Low Ib | LPV821 LPV811, LPV812
Ultrasonic transducer | Optical sensor | Low power Low Ib RRIO | TLV6003
Ultrasonic transducer | Obstruction sensor | Low power Low Ib Wide BW | TLV9061
Application: Smoke detector
Notes: 2