## Slide 1: AMC0311S/R-Q1 vs ADuM4195-1
TI Isolated Converters

## Slide 2: Analog Spec Comparison
AMC0311D/R/S vs AMC1311 vs AMC1311B vs ADuM4195
Parameter | AMC0311R | AMC0311S | AMC1311 | AMC1311B | ADuM4195
Input Voltage Range (V) | 0.13 to 2.25 | 0 to 2.25 | 0 to 2 | 0 to 2 | 0 to 5
Output Type | Single-Ended (Ratiometric) | Single-Ended | Differential | Differential | Single-Ended
Output Bandwidth (typ) (kHz) | 110 | 110 | 220 | 275 | 210
CMTI (min) (kV/µs) | 150 | 150 | 15 | 100 | 150
Nonlinearity (max) (%) | ±0.05 | ±0.05 | ±0.04 | ±0.04 | N/A
Input Offset Voltage (max) (mV) | ±1.5 | ±1.5 | ±9.9 | ±1.5 | 5
Offset Error Thermal Drift (max) (µV/°C) | ±30 | ±25 | ±20 | ±10 | 22 (typ)
Gain Error (max) (%) | ±0.25 | ±0.25 | ±1 | ±0.2 | ±0.5
Gain Error Thermal Drift (max) (ppm/°C) | ±40 | ±40 | ±30 | ±40 | ±42
SNR (typ) (dB) (BW = 100kHz) (*BW = 50kHz) | 70* | 70* | 70.9 | 70.9 | 69
Specified Temperature Range (°C) | -40 to 125 | -40 to 125 | -40 to 125 | -55 to 125 | -40 to 125

## Slide 3: Isolation Spec Comparison
AMC0311D/R/S vs AMC1311 vs AMC1311B vs ADuM4195
Parameter | AMC0311D | AMC0311R | AMC0311S | AMC1311 | AMC1311B | ADuM4195
Isolation Rating | Reinforced | Reinforced | Reinforced | Reinforced | Reinforced | Reinforced
Creepage (mm) | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.3
Clearance (mm) | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.3
AC Working Voltage (VIOWM) (VRMS) | 1500 | 1500 | 1500 | 1500 | 1500 | 1400
DC Working Voltage (VIOWM) (VDC) | 2121 | 2121 | 2121 | 2121 | 2121 | 1980
Transient Overvoltage (VIOTM) (VPeak) (t = 60s) | 7000 | 7000 | 7000 | 7000 | 7000 | 7000
Surge Voltage (VIOSM) (VPeak) | 10000 | 10000 | 10000 | 12800 | 12800 | 8000
Withstand Isolation Voltage (VISO) (VRMS) | 5000 | 5000 | 5000 | 5000 | 5000 | 5000
Notes: AMC1300, AMC1300B are rounded to 2120 instead of 2121