## Slide 1: Precision Amplifiers for Battery management systems
Reference Designs / Collateral
Automotive High-Voltage and Isolation Leakage Measurements Ref. Design
Leakage Current Measurement Ref. Design for determining Insulation Resistance
Collateral
Subsystem: 48V battery current measurement
Subsystem: Isolation leakage measurements
HV Battery
Select OPAMP or Difference amplifier / INA depending on error budget
OPAx388-Q1
Reference Designs / Collateral
Battery current measurements (48V systems) – OPAx388-Q1
  Very high precision for reducing error when measuring lower end of current range with small shunts.
  High gain bandwidth to measure mA to kA range.
  Very low 1/f noise to increase measurement resolution.
Isolation current measurements – OPA320-Q1, INA333-Q1, INA148-Q1
High precision and low gain error with integrated matched resistors to reduce total error, account for shifting chassis GND and reduce BOM cost.
Key amplifier wpecs and hero parts
Reference Designs / Collateral
Device | Supply Range | Vos (mV) (max) | Vos Drift (typ) (uV/ºC) | GBW (MHz) | Slew Rate (V/µs) | Voltage Noise (typ) (nV/) | IBias (typ) (pA)
OPAx388-Q1 Texas Instruments | 2.5V – 5.5V | .005 | .005 | 10 | 5 | 7 | 30
AD8628 Analog Devices | 2.7V – 5.5V | .005 | .002 | 2.5 | 1 | 22 | 30
MCP6V91 Microchip | 2.V – 5.5V | .009 | .017 | 10 | 9.5 | 11 | 2
Device | Supply Range | Vos (mV) (max) | Vos Drift (typ) (uV/ºC) | GBW (MHz) | Slew Rate (V/µs) |  | IBias (typ) (pA)
OPAx388-Q1 Texas Instruments | 2.5V – 5.5V | .005 | .005 | 10 | 5 | 7 | 30
AD8628 Analog Devices | 2.7V – 5.5V | .005 | .002 | 2.5 | 1 | 22 | 30
MCP6V91 Microchip | 2.V – 5.5V | .009 | .017 | 10 | 9.5 | 11 | 2
Key spec competitor analysis
Systems engineer – Scott Gulas Marketing engineer – Jacob Fattakhov
PRAMPS automotive contacts
Leading Spec |