## Slide 1: Precision Amplifiers for DC-DC Converters
Reference Designs / Collateral
Key amplifier specs and hero parts
Key specs for current/voltage/temp. sensing
Current/Voltage sensing
Temperature sensing
Subsystem: Bidirectional converter
TI Confidential - NDA Restrictions
Device Dual Channel | Supply Range | Channel Count | GBW (MHz) | Slew Rate (V/µs) | Vos (mV) (max) | Cost (1ku) (single)
TLVx197-Q1 Texas Instruments | 4.5V – 36V | 1,2,4 | 2 | 3.4 | .6 | $0.468
OPAx388-Q1 Texas Instruments | 2.5V – 5.5V | 1,2 | 10 | 5 | .005 | $1.119
AD862x Analog Devices | 2.7V – 5.5V | 1,2,4 | 2.5 | 1 | .005 | $0.960
TSX71x ST Micro | 2.7V – 16V | 1,2 | 2.7 | 1.3 | .2 | $0.527
Device | Supply Range | GBW (MHz) | Slew Rate (V/µs) | Vos (mV) (max) | Vos Drift (typ) (uV/ºC) | IQ (mA) (typ)
OPAx333-Q1 Texas Instruments | 1.8V – 5.5V | .35 | .16 | .01 | .02 | .017
OPAx317-Q1 Texas Instruments | 1.8V – 5.5V | .35 | .15 | .09 | .05 | .021
NCVx333 On Semi | 1.8V – 5.5V | .3 | .1 | .03 | .03 | .021
Systems engineer – Kartik Sinha Marketing engineer – Jacob Fattakhov
PRAMPS automotive contacts
Use of high switching frequencies requires higher speed amplifiers with fast settling times
Avoid extensive calibration using high precision amplifiers with low voltage offset and offset drift
Dual/Quad channel amps in small form factors save board space
Leading Spec | 

## Slide 2: EE: DC-DC Converters
Primary and Secondary Current/Voltage Sense
  It is important to measure input/output voltage and current to maintain the control loop stable and provide basic set of diagnostics and safety.
Identified EE Subsystems for PRAMPS
A DC/DC converter from high voltage (hundreds of volts) to 12 or 48V is required for powering low-voltage end-equipment’s such as infotainment, power steering, ABS, A/C and lots of others.
This voltage rail not only energizes legacy 12-V devices but also simplifies the design for various low-power EEs because basic isolation is not needed.
What is it?
Hero Devices and Cookbook Circuits
INA148-Q1: +-200V Common-Mode Voltage Difference Amplifier
OPA197-Q1: 36-V, Precision, Rail-to-Rail Input Output, Low Offset Voltage
OPA376-Q1 Precision, Low Noise, Low Iq Operational Amplifier
OPAx188-Q1: 36-V, 0.03µV/C, Low Noise, Rail-to-Rail Output, Zero-Drift Op Amp

## Slide 3: LAMPs in HEV/EV – DC/DC Unidirectional
Reference Designs / Collateral
Hero parts
Function |  | Key LAMP requirement | Devices
Low side current sense on primary and secondary sides |  | Fast settling OPAMP to account for high switching frequencies | OPA607-Q1, OPA365-Q1, TLVx197-Q1
 |  | Budget conscious | TLV9062/4-Q1, TLV9352-Q1
Battery voltage measurements post resistor divider |  | Fast settling OPAMP to account for high switching frequencies | OPA365-Q1, TLVx197-Q1
 |  | Budget conscious | TLV9062/4-Q1, TLV9352-Q1
Post magnetic sensor signal conditioning |  | Budget conscious | TLV9002/4-Q1
OC & OV fault detect with comparators |  | Low offset, fast response, precision integrated reference | TLV9022-Q1, LM2903B-Q1, TLV4011-Q1, TLV6703-Q1
Current/Voltage Sense
Discovery Questions:
Most common switching frequencies used? High speed OPAMPs needed?
Is Isolation leakage measurement done in this system?
Correlation between battery bus voltage measurement error and system efficiency?
Function |  | Key LAMP requirement | Devices
Buffer OPAMP for NTC |  | Budget conscious | TLV9002/4-Q1, LM290xLV-Q1, LM2904B-Q1
 |  | High precision | OPA333-Q1
Thermocouple, 3-wire RTD front end |  | Low power instrumentation amplifier | INA333-Q1
Thermal switch (COMP) |  | Low power, low offset, integrated hysteresis | TLV7041-Q1, TL331B-Q1, LM2903B-Q1
Temperature Sense

## Slide 4: LAMPs in HEV/EV – DC/DC Bidirectional
Reference Designs / Collateral
Hero parts
Function |  | Key LAMP requirement | Devices
Low side current sense on primary and secondary sides |  | Fast settling OPAMP to account for high switching frequencies | OPA607-Q1, OPA365-Q1, TLVx197-Q1, OPA388-Q1
 |  | Budget conscious | TLV9062/4-Q1, TLV9352-Q1
Battery voltage measurements post resistor divider |  | Fast settling OPAMP to account for high switching frequencies | OPA365-Q1, TLVx197-Q1
 |  | Budget conscious | TLV9062/4-Q1, TLV9352-Q1
Post magnetic sensor signal conditioning |  | Budget conscious | TLV9002/4-Q1
OC & OV fault detect with comparators |  | Low offset, fast response, precision integrated reference | TLV9022-Q1, LM2903B-Q1, TLV4011-Q1, TLV6703-Q1
Current/Voltage Sense
Discovery Questions:
Most common switching frequencies used? High speed OPAMPs needed?
Is Isolation leakage measurement done in this system?
Correlation between battery bus voltage measurement error and system efficiency?
Function |  | Key LAMP requirement | Devices
Buffer OPAMP for NTC |  | Budget conscious | TLV9002/4-Q1, LM290xLV-Q1, LM2904B-Q1
 |  | High precision | OPA333-Q1
Thermocouple, 3-wire RTD front end |  | Low power instrumentation amplifier | INA333-Q1
Thermal switch (COMP) |  | Low power, low offset, integrated hysteresis | TLV7041-Q1, TL331B-Q1, LM2903B-Q1
Temperature Sense
v