## Slide 1: High-Side Voltage to Current Converter OPA197
Luis Chioye –ASC - Precision Amplifiers
Notes: .

## Slide 2: OPA2197 High-Side, Current-to-Voltage Converter
Proposed Circuit:
RSet = 5.9kΩ
Vsupply = +12V
RLoad = 2kΩ
ILoad Max = ~5mA
Load Compliance > 10V
Transfer function
Noise < 100mVpp
Slew rate 10%-90%, 2.5mA Step: <4us

## Slide 3: OPA2197 High-Side, Current-to-Voltage Converter
Proposed Circuit:
OPA2197
N-Channel and P-Channel FET
% Error Accuracy is dependent on
Rs1, Rs2, Rs3 resistor tolerance/accuracy.
Rs1, Rs2, Rs3 are 0.5% tolernace resistors

## Slide 4: OPA2197 High-Side, Current-to-Voltage Converter
DC Transfer Function Simulation:
TINA Simulation:

## Slide 5: OPA2197 High-Side, Current-to-Voltage Converter
DC Transfer Function Simulation :

## Slide 6: OPA2197 High-Side, Current-to-Voltage Converter
Total Output Noise Simulation:
At 5-mA output, RLoad = 2kΩ, Vin = 3V, Vout = +10.169V
Vin = 3V
Vout = 10.169V
TINA Simulation:

## Slide 7: OPA2197 High-Side, Current-to-Voltage Converter
Total Output Noise Simulation:
At 5-mA output, RLoad = 2kΩ, Vin = 3V, Vout = +10.169V

## Slide 8: OPA2197 High-Side, Current-to-Voltage Converter
Transient Simulation:
Vin = 100mV to +1.6V
Iout = 339µA to 2.712mA (~2.5mA step)
Vin = 100mV to +1.6V
Vout = 0.339V to 5.424V
Iout = 339µA to 2.712mA
(~2.5mA step)
TINA Simulation:

## Slide 9: OPA2197 High-Side, Current-to-Voltage Converter
Transient Simulation:
Vin = 100mV to +1.6V
Iout = 339µA to 2.712mA (~2.5mA step)
Vout = 0.339V to 5.424V
V-Load (90%) = ~4.915V @ 4.403µs
V-Load (10%) = ~0.847V @ 2.648µs
Slew Time = 1.755µs

## Slide 10: OPA2197 High-Side, Current-to-Voltage Converter
Transient Simulation #2:
Vin = 0mV to +1.5V
Iout = ~0µA to 2.542mA (~2.5mA step)
Vin = 100mV to +1.6V
Vout = ~0V to 5.085V
Iout = ~0µA to 2.542mA
(~2.5mA step)
Note:
When Vin = 0-V, Iout = 0mA
Stage 2 output U2 will be on the positive rail,
Response of circuit takes microseconds due to op-amp being on the rail.
This is not an issue if let Vin start as some small voltage. Vin(min) = ~10mV

## Slide 11: OPA2197 High-Side, Current-to-Voltage Converter
If Vin = 0V, Iout = 0mA,
Stage 2 transistor is off,
Stage 2 Op-Amp is on the positive rail
Delay ~17µs for circuit to respond.
V-Load (90%) = ~4.576V @ 21.858µs
V-Load (10%) = ~0.508V @ 19.457µs
Slew Time = 2.4µs
Delay due to Stage 2 on the rail

## Slide 12: Thanks for your time!

## Slide 13
Important notice and disclaimer
TI PROVIDES TECHNICAL AND RELIABILITY DATA (INCLUDING DATASHEETS), DESIGN RESOURCES (INCLUDING REFERENCE DESIGNS), APPLICATION OR OTHER DESIGN ADVICE, WEB TOOLS, SAFETY INFORMATION, AND OTHER RESOURCES “AS IS” AND WITH ALL FAULTS, AND DISCLAIMS ALL WARRANTIES, EXPRESS AND IMPLIED, INCLUDING WITHOUT LIMITATION ANY IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE OR NON-INFRINGEMENT OF THIRD PARTY INTELLECTUAL PROPERTY RIGHTS.
These resources are intended for skilled developers designing with TI products. You are solely responsible for (1) selecting the appropriate TI products for your application, (2) designing, validating and testing your application, and (3) ensuring your application meets applicable standards, and any other safety, security, or other requirements.
These resources are subject to change without notice. TI grants you permission to use these resources only for development of an application that uses the TI products described in the resource. Other reproduction and display of these resources is prohibited. No license is granted to any other TI intellectual property right or to any third party intellectual property right. TI disclaims responsibility for, and you will fully indemnify TI and its representatives against, any claims, damages, costs, losses, and liabilities arising out of your use of these resources.
TI’s products are provided subject to TI’s Terms of Sale or other applicable terms available either on ti.com or provided in conjunction with such TI products. TI’s provision of these resources does not expand or otherwise alter TI’s applicable warranties or warranty disclaimers for TI products.