## Slide 1: High output power under 915 MHz FCC regulations without FHSS
Digital modulation

## Slide 2
FCC allows high output power under the ”digital modulation” requirements
Max output power is then (without hopping) up to 1W (+30dBm)
  FCC requirements for digital modulation:
  Minimum 6dB TX bandwidth needs to be at least 500kHz
  Peak power density in any 3kHz bandwidth needs to be below +8dBm
This is an attractive regulation for a low power protocol where frequency hopping is not attractive/needed.
The same protocol – and output power, can be used for ETSI (Europe++) and FCC (USA++)
CC1200 has a special processing gain feature that will improve the sensitivity/range under these regulations
  Challenge: Get good sensitivity for a wide 500 kHz channel
  Solution: Use processing gain, 4 chips per bit – this digital feature is integrated into the CC1200 MODEM as well as packet engine. It is just to enable the feature in the register [7:6] modem_mode and the chip handles the rest.
CC1200 for FCC and “digital modulation”

## Slide 3
US + EU solution – same hardware, same software:
  Europe 868.3 MHz with 50kbit/s and +14dBm is a popular setting since it is a good trade off between data rate and sensitivity.
  +14dBm is maximum output power allowed in most 863-870MHz bands.
  Using processing gain in CC120x (4 chips per bit) under FCC regulations, the CC1200 can for the US market be configured to transmit 200kbit/s, but the over the air data rate will be 50kbit/s (200k/4) – no change in software is needed (apart from a few register changes – just constants). Same output power can be used +14dBm.
US – best possible range without frequency hopping
  Frequency hopping is not ideal for low power, low duty cycle systems due to the energy spent on synchronizing the hopping. As an alternative, ”digital Modulation” can be used for applications such as remote start, various wireless sensors or as the starting frequency for synchronization in a frequency hopping solution.
  Using processing gain, the sensitivity and selectivity/robustness is increased – thus giving improved range.
Examples

## Slide 4
To be “wide enough” to cover 500kHz (6dB limit) in TX, a relatively high data and deviation has to be used:
  200kbit/s GFSK, +-180kHz dev
    This gives a bandwidth of 514kHz (limit is minimum 500kHz)
    With maximum output power (+14dBm) , the Power Spectral Density is +4.8dBm (limit is max +8dBm)
    Note that higher output power with an external PA is possible, but then the data rate has to be increased.
CC1200 Sensitivity measurements (555kHz RX BW. 1% BER):
  Average performance over 6 CC1200, 868/915MHz EMs, 3V, 25 degrees
  No processing gain (“regular” GFSK at 200kbit/s): - 101.5 dBm
  With processing gain (4 chips per bit, 50kbit/s): -104.75 dBm – an improvement of 3.25dB
Link budget comparison:
  Europe (ETSI): 50 kbps. +14 dBm and -110 dBm sensitivity: Link budget = 124 dB
  USA (FCC 5.247): 200 kbps with code gain (50 kbps throughput): +14 dBm and -105 dBm sensitivity. Link budget = 119 dB
  USA (FCC 15.249): 50 kbps. -1.25 dBm (no hopping or digital modulation) and -110 dBm sensitivity. Link budget = 109 dB
Digital Modulation (FCC 15.247) gives a 10dB increase in link budget compared to not using any spread spectrum technology (FCC 15.247)
CC1200 performance for “digital modulation”