## Slide 1: TI CC2520 and differential load impedance Question
Per Fager NIBE, Sweden
Per Sandrup Halmstad University, ECH, Sweden
20200402

## Slide 2: CC2520 and optimal load (load pull analysis)
From an email conversation between Per Fager, NIBE Sweden and Richard, TI.
TI stated that the load should be close to 70+j95 ohm in the band of 2405 – 2480MHz.
My (Per S) interpretation is that the load seen differential from CC2520 pin pair 17 and 19, is 70+j95 ohm

## Slide 3: The TI Eval board and CC2520
To ensure if we are on the right track from an differential impedance point of view.
A TI-Eval board was determined to be used to measure the differential impedance created by the discrete on the PCB.
A 3-port mixed mode s-parameter analysis was carried out.
The result is 39+j57-ohms at 2405MHz
This is a bit different to 70+j95-ohms
What is the explanation here?

## Slide 4: The measurement setup and calibration
To attached the network analyser at the pads for pin 17 and 19 of the CC2520, 2 semi-rigids are used.
The network analyser is calibrated using an ECAL-kit (3-ports), then an additional auto-port extension is carried out for the 2 ports that connected to the semi-rigids.

## Slide 5: The End