## Slide 1: MSP430FR6043 MCU
MSP-FET:
Metrology solution for Gas with best performance & low power
  < 1ns Zero Flow Drift
  < 4ns Standard Deviation
  <20 uA average measurement current
Ultrasonic Sub-system ( Integrated High Performance SD-ADC, Pulse Position Generator & Integrated PHY ) with Software Library Support
LEA ( Low Energy Accelerator ) for optimizing power
MTIF ( Metering Test Interface Module ) running in Sleep Mode
64 & 80-pin package options
Features/Benefits
Ultrasonic Flow Meters
( Gas, water & Heat )
Distance Measurement
Target Applications
USS Software Library, GUI
MSP430Ware
Software
MSP-TS430xxxx
- 80-pin target socket board
MSP-FET: Flash emulation tool
Occupancy Detectors
Level Sensing
Tools
MSP430FR6043
Temperatures | -40°C to 85°C
Up to 64 KB FRAM (with segment protections
for code/data)
Real-Time Clock with calendar mode
Serial Interface
Memory
Power & Clocking
Debug
Embedded Emulation
Watchdog Timer
USS Module
( PPG, PGA
12 bit 8MSPS SDHS )
12bit SAR ADC, COMP
1× 16 bit TA w/ 5CC regs
1 × 16 bit pure TA w/ 3CC
LFXT, HFXT
PMM with BOR, POR,PUC &SVS
DCO, REFO, VLO
FLL
2× I2C or SPI
4 × UART + IrDA or SPI
Up to 64 GPIOs
64-pin QFN / LQFP
80-pin LQFP
Bootstrap Loader
Real-time JTAG/SBW
CRC16 / 32
8KB Shared RAM for LEA
Up to 12KB SRAM
Packages
Analog
MPY32
System Module
IOs
Voltage | 1.8V-3.6V
MSP430FR6043
16-bit
Up to 16 MHz
Data Protection
Timers
  Gas Meter EVM
LEA
Data Processing
MTIF in LPM3.5 mode
Upto 248 Segments
LCD Driver
TI Information - Selective Disclosure
Notes: Target Applications, (Make Tools/Software -> Ecosystem)
MSP-FET: