下午好，

我司目前使用的Instaspin电机控制套件《DRV8301-69M-KIT》（Motor Drive and Control aolutions）如下图：

The Instaspin motor control kit called <DRV8301-69M-KIT> (Motor Drive and Control aolutions) is shown below:

目前使用的软件的是Code Composer Studio Version: 11.0.0.00012 版本。

The current software used is Code Composer Studio Version: version 11.0.0.00012.

motorware_1_01_00_18里面的相关源文件/库文件

Related source / library files in motorware_1_01_00_18

现在遇到的问题：

The problem that I have encountered right now:

在根据《instaspin_labs》文档做lab01的工程，出现AD采样部分数据都是0，如图：

按照手册Lab01正常下载后得到LED闪烁

In the lab01 project according to the instaspin_labs document, the AD sampling data is all 0, as shown in the figure: Follow manual Lab01 and get LED flashing

但是出现AD采样部分数据都是0

However, part of the AD sampling data is 0

具体细节 新建工程和官方工程的差别：

Specific Details: Differences between new construction projects and official construction projects:

我根据Lab01工程文件新建立了一个项目（如图）：

I built a new project from the Lab01 engineering document (see picture):

原工程文件如图：使用的是不带fpu的lib

The original engineering document: using lib without fpu

调试发现问题在这，但是不知道为啥，也没解决措施！！！如下图

Debug found the problem in here, but do not know why, also have no solution!!!

as illustrated in following figure

但我测试IQmath_fpu这个lib，是能正常计算值的如下图：在新工程里面使用

But I tested the IQmath_fpu lib, which can normally calculate the value below: used in the new project

Results：

对比原官方lab01计算的dcBus

Compare the dcBus calculated from the original official lab01

这里我确认调用IQmath_fpu32.lib应该配置是正确的，但是却不清楚为啥原工程调试能把AD值转化出来，新建工程却不行？？？

Here I confirm that the call to IQmath_fpu32.lib should be configured correctly, but it is not clear why the original project debugging can convert the AD value out, but the new project is not good???

# Text boxes

The compilation is successful, with two more prompts

I copied the new project file

Here I changed the library file to bring the “fpu”

The problem is here

This is wrong by assigning the voltage_sf of to the corresponding voltage_sf in halHandle, and this specific function is wrong by calculating the float in the Q format

Modify, just to confirm that the IQmath_fpu configuration is ok

Official lab01 direct download to development board dcBus has value display

Values remained close to those calculated using IQmath_fu32.h