## Slide 1: MCAN Filtering and RX Configuration
TI – EP – ASM-IND
Zackary Fleenor

## Slide 2: Introduction
Overview of MCAN module
  Key Features
    Conforms with CAN Protocol 2.0 A, B and ISO 11898-1:2015
    Full CAN FD support (up to 64 data bytes); 1Mbps nominal bit rate; 8Mbps data bit rate
    AUTOSAR and SAE J1939 support
    Up to 32 dedicated transmit buffers
    Configurable Transmit FIFO (up to 32 elements)
    Configurable Transmit queue (up to 32 elements)
    Configurable Transmit Event FIFO (up to 32 elements)
    Up to 64 dedicated receive buffers
    Two configurable receive FIFOs (up to 64 elements each)
    Up to 128 filter elements

## Slide 3: MCAN Block Diagram

## Slide 4: Implementation Details
Acceptance filtering mechanisms
  Filtering Features
    Hardware-based acceptance filtering Two filter sets: standard and extended identifiers Multiple filter configurations are available Configurable for acceptance or rejection Individual filter enable/disable support
  Filter Types
    Range filter [from ID1 to ID2] Filter for dedicated message IDs [ID1 and ID2] Classic bit mask filter [ID1(MASK) and ID2] Global filter configuration [Accept/Reject Remote/Data Frames]

## Slide 5: Acceptance Filtering Capabilities
Key filtering features and mechanisms
  Hardware-based filtering support
  Standard and Extended identifier filter sets
  Range, Dedicated ID, and Bit mask filtering
  Individual filter enable/disable
  Sequential filter checking

## Slide 6: Standard ID Filter Flow

## Slide 7: Extended ID Filter Flow

## Slide 8: Standard ID Filter Configuration

## Slide 9: Filter Configuration Options
Available filter types and configurations
  Range filter [from IDx to IDy]
  Dual ID filter support
  Classic bit mask filtering
  Acceptance or rejection filtering
  Assignment to RX Buffers or FIFOs

## Slide 10: MCAN Global Filter
AM261x MCU+ SDK: MCAN_GlobalFiltConfig Struct Reference

## Slide 11: MCAN_GlobalFilter Configuration
/* Global Filter Configuration parameters. */
.filterConfig.rrfe = false,
.filterConfig.rrfs = false,
.filterConfig.anfe = 0,
.filterConfig.anfs = 0,

## Slide 12: MCAN StdMsgID Filter
AM261x MCU+ SDK: MCAN_StdMsgIDFilterElement Struct Reference

## Slide 13: MCAN_StdMsgIDFilterElement Configuration
MCAN_StdMsgIDFilterElement exFilterConfig0 =
{
.sfid1 = 0U,
.sfec = MCAN_STD_FILT_ELEM_BUFFER,
.sfid2 = 15U,
.sft = MCAN_STD_FILT_TYPE_RANGE,
};

## Slide 14: MCAN ExtMsgID Filter
AM261x MCU+ SDK: MCAN_ExtMsgIDFilterElement Struct Reference

## Slide 15: MCAN_ExtMsgIDFilterElement Configuration
MCAN_ExtMsgIDFilterElement exFilterConfig0 =
{
.efid1 = 670U,
.efec = MCAN_EXT_FILT_ELEM_BUFFER,
.efid2 = 670U,
.eft = MCAN_EXT_FILT_TYPE_RANGE,
};

## Slide 16: MCAN Message RAM – RX Configuration Options
Up to 64 Rx buffers and two Rx FIFOs can be configured in the Message RAM.
RX FIFO0 and RX FIFO1 Start Address: defines the start address of Rx FIFOs in message RAM.
Number of RX FIFO0 and RX FIFO1 Elements: each Rx FIFO can be configured to store up to 64 received messages.
RX FIFO0 and RX FIFO1 Watermark: the Rx FIFO watermark can be used to prevent an Rx FIFO overflow. If the Rx FIFO fill level reaches the Rx FIFO watermark, then an interrupt flag MCAN_IR.RF0W/ MCAN_IR.RF1W is set.
RX FIFO0 and RX FIFO1 Operation Mode:
  Rx FIFO Blocking Mode: the Rx FIFO blocking mode is the default operation mode for the Rx FIFOs. If an Rx FIFO full condition is reached, then no further messages are written to the corresponding Rx FIFO until at least one message is read out and the Rx FIFO Get Index is incremented.
  Rx FIFO Overwrite Mode: when an Rx FIFO full condition is reached, the next accepted message for the FIFO overwrites the oldest FIFO message.
RX FIFO0 and RX FIFO1 Element Size: defines the Rx FIFO element size.
RX Buffer Start Address: defines the start address of Rx buffer in message RAM.
RX Buffer Element Size: defines the Rx buffer element size.

## Slide 17: MCAN Message RAM Configuration

## Slide 18: MsgRAM ConfigParams
AM261x MCU+ SDK: MCAN_MsgRAMConfigParams Struct Reference

## Slide 19: AM261x MCU+SDK MCAN Configuration Example

## Slide 20: Questions?