## Slide 1
Driver Lib based CCS Code Development
(Independent Project)

## Slide 2
Create a New Project (Independent Project)
To make an independent Project, all the required source files must be included locally in the “created project”.
Avoid external dependencies on C2000ware paths
Create a New Project
Make a new workspace for the new project
After making the new workspace, Reset perspective as shown in the figure below

## Slide 3
CCStudio Set-Up
Create new project in CCS Project
File >> New >> CCS Project

## Slide 4
Set the Target
Target : TMS320F28379D
Connection: Texas Instrument XDS100v2 USB Debug Probe
Select Project Template: Empty Project(with main.c)
Project Name : as desired
Click Verify: it will show succeeded.
Click Finish

## Slide 5
Make Folders
Made folders as shown below
  CMD
  DRIVERLIB
    INCLUDE
    SOURCE
  INCLUDE
  SOURCE

## Slide 6
Transfer Device support Files : Header Files
C2000Ware_5_04_00_00\device_support\f2837xd\headers\include
workspacefolder\Project_IO\INCLUDE
Copy all header files from C2000ware and paste in the project INCLUDE folder
Copy
Paste

## Slide 7
Transfer Device support Files : Header Files
Copy all header files from C2000ware and paste in the project INCLUDE folder
C2000Ware_5_04_00_00\device_support\f2837xd\common\include
Workspace Folder >>Project Folder >> INCLUDE
Copy
Paste

## Slide 8
Transfer Device support Files : Source Files
C2000Ware_5_04_00_00\device_support\f2837xd\header\source
Workspace Folder >>Project Folder >> SOURCE
Copy
Paste

## Slide 9
Transfer Device support Files : Source Files
Copy the linker file “F2837xD_RAM_lnk_cpu1.cmd” from the address shown and paste in the project’s SUPPORT folder in driverlib folder
C2000Ware_5_04_00_00\device_support\f2837xd\common\source
Workspace Folder >>Project Folder >> SOURCE
Copy
Paste

## Slide 10
Transfer Device support Files : CMD
C2000Ware_5_04_00_00\device_support\f2837xd\common\CMD
Workspace Folder >>Project Folder >> CMD
Copy
Paste

## Slide 11
File Confirmation in the Project Folder

## Slide 12
Delete RAM and FLASH file
Delete this RAM and Flash file

## Slide 13
Transfer Driver Library files : Header files
C2000Ware_5_04_00_00\driverlib\f2837xd\driverlib
Workspace Folder >>Project Folder >> DRIVERLIB >> INCLUDE
Copy all Header file (.h)
Paste

## Slide 14
Transfer Driver Library files : Source files
C2000Ware_5_04_00_00\driverlib\f2837xd\driverlib
Workspace Folder >>Project Folder >> DRIVERLIB >> SOURCE
Copy all Source file (.c)
Paste

## Slide 15
Add Predefined Symbols
“CPU1” is added

## Slide 16
Include Path Configuration
Project’s Driver library and device support header files path are added in the Include Paths

## Slide 17
Build
After Building the project, I got following errors.

## Slide 18
Thank You