## Slide 1
CCS Set-up for TMS320F28379D

## Slide 2
The following software are installed and these are downloaded from ti official website
ControlSuite
C2000Ware
CCStudio Version: 12.8.1.00005
Independent Project Set-Up Process for CCS

## Slide 3
CCStudio Start-Up
Create New workspace for new project
Name the workspace and save in your main workspace folder, as shown below in the figure
After making the new workspace, Reset Perspective as shown below in the figure

## Slide 4
CCStudio Start-Up
Create new project in CCS Project

## Slide 5
CCStudio Start-Up

## Slide 6
Create Folder In The Project
Folder INCLUDE
Folder CMD
Folder SOURCE
Verify: Folders are in The Project

## Slide 7
Importing lib files into the Project
Control SUITE >> Device support
Workspace Folder
Example_6

## Slide 8
Importing lib files into the Project
Control SUITE >> Device support >>F2837xD>>v210
Workspace Folder
Example_6

## Slide 9
Importing lib files into the Project
Control SUITE >> Device support > F2837xD > v210 > F2837xD_header > Include
Workspace Folder >> INCLUDE
Copy
Paste

## Slide 10
Importing lib files into the Project
Copy
Paste
Workspace Folder >> INCLUDE
Control SUITE >> Device support > F2837xD > v210 > F2837xD_Common> include

## Slide 11
Importing lib files into the Project
Workspace Folder >> SOURCE
Control SUITE >> Device support > F2837xD > v210 > F2837xD_Common> source
Copy
Paste

## Slide 12
Importing lib files into the Project
Workspace Folder >> SOURCE
Control SUITE >> Device support > F2837xD > v210 > F2837xD_headers > source
Copy
Paste

## Slide 13
Importing lib files into the Project
Control SUITE >> Device support > F2837xD > v210 > F2837xD_common > cmd
Workspace Folder >> CMD
Copy
Paste

## Slide 14
Importing lib files into the Project
Control SUITE >> Device support > F2837xD > v210 > F2837xD_headers > cmd
Workspace Folder >> CMD
Copy
Paste

## Slide 15
Project Files Confirmation
Confirm these project files present in the project Folder
Delete this RAM & FLASH file

## Slide 16
Add Predefined symbol_1
Predefined “CPU1”
Predefined “_LAUNCHXL_F28379D”

## Slide 17
Include Path Directory
1
2
3
4

## Slide 18
Build the code

## Slide 19
Errors After Building the Project

## Slide 20
Include the Path Directory
The two path directories are added

## Slide 21
Errors After Building the Project
After adding the path directories, following errors comes up

## Slide 22
Thank you