## Slide 1: Missing AQ Event on Sync
Picture of reproduced error with signal names, and AQ settings
ePWM | CAU | CBU | CAD | CBD | ZRO
1A | Set |  |  | Clear | Clear
3A | Set | Clear |  |  | Clear
3B |  |  | Clear | Set | Clear
CAU
CBD
CAU
CBU
CAD
CBD
ZRO
ePWM1A
ePWM3A
ePWM3B
SYNCOUT ZRO Event ePWM1
Trigger setting:
  Pulse width > 100us means short occurring on ePWM3B

## Slide 2: Analysis on Missing AQ Event on Sync
ePWM | CAU | CBU | CAD | CBD | ZRO
1A | Set |  |  | Clear | Clear
3A | Set | Clear |  |  | Clear
3B |  |  | Clear | Set | Clear
CAU
CBD
CAU
CBU
CAD
CBD
ZRO
Analysis of waveforms:
After sync even, ePWM3 starts to count up is shown with the TBCTR illustration.
CAD event is never reached before the sync event from ePWM1
Resolution: Updating counter direction for ePWM3 after sync to be count down instead of count up solves the issue.
ePWM1A
ePWM3A
ePWM3B
SYNCOUT ZRO Event ePWM1
TBCTR
CTR DIR = UP

## Slide 3: Resolution & Summary for missing AQ event on Sync
Resolution:
Disabled PHEN for ePWM1
  EPwm1Regs.TBCTL.bit.PHSEN = TB_DISABLE;
Set PHSDIR to count down for ePWM3
  EPwm3Regs.TBCTL.bit.PHSDIR = TB_DOWN;
Summary:
Trigger setting is never reached on scope
Outputs are running normal