## Slide 1: Differences UCC28063 and UCC28061
2-level EA gain, no slew-rate correction current
    lower 50uS gM allows lower compensation component values
    higher 250uS gM replaces slew-rate correction for fast response
  internal 2kΩ pull-down on LOW_OV, soft-start
  20mV full-soft-start enable threshold
  2-level soft-start currents, 5.9V end-of-ss threshold
  -200mV when in two-phase mode (same as -060/-061)
  -167mV when in single-phase mode

## Slide 2: Differences UCC28063 and UCC28061
VSENSE: two, higher OVP thresholds
  LOW_OV @ +8%, tugs COMP down with 2kΩ, clears @ +6%
  HIGH_OV @ +11%, shuts off gate-drive, clears @ +6%
  Full-soft-start on: HVSEN-OVP, Brownout (after 440ms), VSENSE disable, UVLO, Thermal-shutdown, TSET fault, CS fault
  100ns blanking on ZCD inputs

## Slide 3: Differences UCC28063 and UCC28061
VINAC: dropout detection
  0.35V threshold, 5.3ms delay before action, 0.71V immediate clear
  suspend COMP voltage, add 4uA pull down current
New fault protection added:
  TSET has open- and short-circuit fault protection
  CS has open-circuit fault protection