## Slide 1: Snubber Selection for Converters
Apply Load to a converter and measure resonant frequency (f1) on switch node transition
Add a reasonable an amount of capacitance (CP2) whose value is somewhere between COSS of the low side FET and 2COSS to the switch node to ground and measure the resonant frequency again (f2).
The result is two equations and two unknowns (CP1 and LP)
The next step is to find an RS value which will slightly over-damp the LRC resonance by setting Q roughly equal to 0.9
The power dissipated in the snubber resistor will be ½ CV2 for turn on and ½ CV2 for turn off:
Notes: This is the first order approximation process for finding snubber values for a buck converter. Proper measurement techniques to reduce parasitics are necessary when measurement switch node resonant frequencies.
The first step is to measure the ringing frequency on the switch node, f1. Then add an external capacitor from the switch node to ground, CP2, with a value between COSS (from the FET data sheet) and 2COSS. Measure the new resonant frequency, f2.
The resulting two equations can then be solved for the two unknowns, LP and CP1.
The next step is to determine the approximate value of RS which will slightly over-damp the LRC resonance by setting Q equal to 0.9. The equation for Q can then be solved for RS.
One can see that the added capacitance is the directly proportional to the total loss in the snubber. There may be an iterative process required to find a value that minimizes losses and provides adequate damping of the ringing on the switch node.
RS and CP2 can be further optimized by experimentation—increase CP2 slightly and decrease RS.
Snubbers are more effective the closer you can physically get them to the die voltage which you trying to snub, so the RC should be placed as close to the drain-to-source on the low side FET in a buck as possible. Make sure to adequately size the resistor to handle the power dissipation. The capacitor will not dissipate any notable amount power.
The power dissipated in the snubber resistor is approximately
P = CP2VINPUT2FSWITCHING.
For an example power calculation, assume CP2 = 600 pF, VINPUT = 12 V, FSWITCHING = 1 MHz, then P = 86 mW.