## Slide 1: 2 x PMP22477 Power Sharing & Limiting Test - Pictures
50 V
TPS23881EVM x 1
Two 2-paris ports (30 W each) were used
PMP22477 x 2
Shorted the output sides; no dedicated oring circuit
Test Setup:

## Slide 2: 2 x PMP22477 Power Sharing & Limiting Test - 1
  VDD - VSS = 50 V
  Vout = 12 V
  Iout = 1.8 A
  Plmt(PD1) = 25.5 W
  Plmt(PD2) = 25.5 W
Test Condition: Insert PD2 when PD1 is exiting
Vout
IPD1 = 460 mA
IPD1 = 260 mA
IPD2 = 240 mA
50 V

## Slide 3: 2 x PMP22477 Power Sharing & Limiting Test - 2
  VDD - VSS = 50 V
  Vout = 12 V
  Iout = 1.8 A
  Plmt(PD1) = 25.5 W
  Plmt(PD2) = 25.5 W
Test Condition: Remove PD2 when PD1 & PD2 are both exiting
Vout
IPD1 = 460 mA
IPD1 = 260 mA
IPD2 = 240 mA
50 V

## Slide 4: 2 x PMP22477 Power Sharing & Limiting Test - 3
  VDD - VSS = 50 V
  Vout = 12 V
  Iout = 1.8 A -> 3.6 A
  Plmt(PD1) = 25.5 W
  Plmt(PD2) = 25.5 W
Test Condition: Increase Iout when PD1 & PD2 are both exiting
Vout
IPD1 = 450 mA
IPD1 = 240 mA
IPD2 = 240 mA
50 V
IPD2 = 460 mA

## Slide 5: 2 x PMP22477 Power Sharing & Limiting Test - 4
  VDD - VSS = 50 V
  Vout = 12 V
  Iout = 3.6 A -> 1.8 A
  Plmt(PD1) = 25.5 W
  Plmt(PD2) = 25.5 W
Test Condition: Reduce Iout when PD1 & PD2 are both exiting
Vout
IPD1 = 440 mA
IPD1 = 240 mA
IPD2 = 240 mA
50 V
IPD2 = 440 mA

## Slide 6: 2 x PMP22477 Power Sharing & Limiting Test - 5
  VDD - VSS = 50 V
  Vout = 12 V
  Iout = 1 A -> 2.4 A
  Plmt(PD1) = 25.5 W
  Plmt(PD2) = 13 W
Test Condition: Increase Iout when PD1 & PD2 are both exiting; PD2 recaches power limitation
Vout
IPD1 = 120 mA
IPD1 = 390 mA
IPD2 = 240 mA
50 V
IPD2 = 120 mA