## Slide 1
CH1: VSYS I
CH2: VSYS V
주기: 417kHz
CH1: Current 1.97A max, -800mA min
CH2: VSYS 14.6V rms
13.5V min
CH1: Peak Current period: 15.5mS
duty ratio : around under 1%
□ Input Current
CH1 Yellow : Input Current
1.97A peak, -800mA min
CH2 Green : Input Voltage 14.6V rms
CH4 Red : Output Voltage
Q1 : Is narrow-band high current normal operation?
Is there a way to reduce narrow-band impulse current?
When I changed R_sens from 0.5 ohm to 2 ohm, average
current was reduced, but peak current was not reduced at on time.
(※ Due to the narrow-range shock current, it is affecting the adjacent power and ground. In the next step PCB, the input power and ground will be separated, but if there is a way to improve the components around the TPS923652, please let me know.)
Q2 : If the input current in the form of a sine wave is wrong,
please tell me how to improve it.

## Slide 2
□ PWM Duty ratio and start-Up current for reference
□ PWM Start
. PWM High : 110uSec,
(PWM High width : 110uS ~ 192uS)
. Period : 15.5mSec
ⓒ
ⓑ
ⓐ
ⓐ
ⓑ
Yellow: Input current (R_sens_0.5 ohm)
period : 2.4uSec(417kHz)
105uS
ⓒ
ⓐ
122~158.4~192uS
1st PWM Pulse
2nd PWM Pulse
2-Sec On
2-Sec Off
Vout (Desired Output )
Yellow: Input current (R_sens_2 ohm)

## Slide 3
□ TPS923652 schematic (After)
12V~ 16.8V
L13
MSS6132-223MLC
22uH shield 20% 1.9A (from 110mA)
DCR 158mΩ
R246
0.5 Ω /1608
DRV8871
LOAD
560kΩ
VM
OUT1
OUT2
2S off
1S rampUp
1s
1S rampUp
A
Current Probe
4.7uF 25V

## Slide 4
C171
C180
C169
R246
R276
C189
C172
C170
R248
R247
C173
C165
C164
C166
R249
R257
L13
D12
□ TPS923652 PCB DG (Before)
12V~ 16.8V
Issue : The switching noise generated in the currently designed PCB is affecting other logic, so I would like to modify it with Ti's guide in the next step PCB version.
Requests: May I have your recommended values ​​for
- R_COMP, C_COMP, C_DAMP
- R_SENS, C_SENS.2.
3. Our design spec
- Vin: 12~16.8V.
- Vout: 40V.
- The output current is under 100mA excluding the output capacitor charging current,
and there is no need for current limit.