## Slide 1: TPS26600 Parallel Operation
Venkata Nandam
Power Switches
Feb 2017

## Slide 2: 3A - TPS26600 eFuse Schematic

## Slide 3: Turn on with VIN
Test Conditions : Vin=24V, 3A Resistive Load, Cout = 47uF
eFuse total Input current
CH1 FLT\ is only shown here
Output voltage soft starts in 5ms with 47nF dVdT cap

## Slide 4: Turn on with SHDN\
Test Conditions : Vin=24V, 3A Resistive Load, Cout = 47uF
eFuse total Input current
SHDN\ of CH1 used to start 3A eFuse (Another channel SHDN\ pin can also be used)
Output voltage soft starts in 5ms with 47nF dVdT cap

## Slide 5: Current Sharing During Steady State
Test Conditions : Vin=24V, 0-3A Constant Current Load, Cout = 47uF
Chart: Load Current Sharing in Efuses
| 0 | 0.5 | 1.0038 | 1.4999 | 2.0065 | 2.5011999999999999 | 3
CH1 | 0 | 0.253 | 0.5045 | 0.7522 | 1.009 | 1.2537 | 1.5017
CH2 | 0 | 0.247 | 0.4993 | 0.7477 | 0.9975 | 1.2475 | 1.4988

## Slide 6: Over Load Response
Test Conditions : Vin=24V, 6Ω Resistive Load, Cout = 47uF
eFuse total Input current regulates to 3.2A during over load
Output voltage drops due to load current regulation
Thermal shutdown auto-retry duration

## Slide 7: Output Continuous Short-circuit Response
Test Conditions : Vin=24V, 0Ω Resistive Load, Cout = 47uF
eFuse total Input current regulates to 3.2A during short circuit
Output drops to zero due to
output continues short-circuit
Thermal shutdown auto-retry duration

## Slide 8: Response at the instance of Short-circuit
Test Conditions : Vin=24V, 0Ω Resistive Load, Cout = 47uF
Total eFuse Input current regulates to 3.2A during short circuit
Output immediately drops to zero due to
short-circuit
FLT\ of both channels asserts low to indicate fault

## Slide 9: Recovery from Short-circuit Response
Test Conditions : Vin=24V, 0Ω Resistive Load, Cout = 47uF
eFuse supports full load 3A during recovery
Output soft starts
after short-circuit release
Thermal shutdown auto-retry duration

## Slide 10: Load Step Response
Test Conditions : Vin=24V, 0A to 3A Resistive Load, Cout = 47uF
eFuse supports full load step from 0A to 3A
No output voltage drop

## Slide 11: Resources
Achieve 20-A Circuit Protection and Space Efficiency Using Paralleled eFuses
http://www.ti.com/lit/an/slva836/slva836.pdf
Calculators, Spice models
http://www.ti.com/product/TPS2660/toolssoftware
Download EVM user’s guide
http://www.ti.com/tool/tps26600-02evm