## Slide 1: TPS55288 EVM Layout Guideline
SR-BCC
Sep, 2024

## Slide 2: Power Components Placement
Input capacitors are placed close to the buck-leg MOSFETs.
Output capacitors are placed adjacent to the TPS55288’s VOUT pin and PGND pin.
The main inductor L1 is placed between the buck-leg MOSFETs and the TPS55288 silicon. The SW node is poured with small copper plane.

## Slide 3: Driver Circuit Routing
Low-Side-FET Drive Traces Routing
High-Side-FET Drive Traces Routing
Kelvin – connecting the gate drive return traces directly to the respective MOSFET sources minimize common-source inductance. To minimize gate-loop area, gate and source traces are routed side by side as differential pairs.
The gate drive resistors should be placed close to the gate terminal of each MOSFET.

## Slide 4: Output Current Sense Traces Routing
Output-Current-Sense Traces Routing
The traces were routed as a tightly-coupled differential pair from the shut resistor to the IC, which can enhance the noise immunity and the accuracy. Place the current-sense filter capacitor close to the IC.

## Slide 5: AGND-PGND Connection
Add enough vias around the output cap.
AGND and PGDN pour separately.
Add 3-4 vias around the GND net of the VCC cap.
GND copper plane for the FB network and the compensation network – small island, separate with the power GND at top layer.
The VCC capacitor should be placed as close to the IC as possible.

## Slide 6: Power and GND Plane Design
Place a whole layer GND copper plane under the switching loops establish a passive shielding for the circuit. -> EMI
Add thermal vias beneath the TPS55288 connecting PGND pin and VOUT pin to the PGND plane and a large VOUT area separately. -> Thermal
Add more vias close to VOUT pin and PGND pin to connect with VOUT plane and PGND plane separately.
Add one 0.1uF/0402 cap at the bottom layer to minimize the Boost power loop.
VOUT
GND
VOUT
GND