## Slide 1: Automotive Hotrod and Wettable Flanks Packaging Advancements
Perry Tsao
Systems and Applications Manager
SVA-PPS-PRS (Performance Regulator Solutions)

## Slide 2: Agenda
Overview of Automotive Hotrod and Wettable Flanks
Performance benefits of Automotive Hotrod
Layout techniques to minimize EMI
Best practices for thermal layout of Hotrod devices

## Slide 3: Automotive Hotrod and Wettable Flanks

## Slide 4: PACKAGE COMPARISON
STD. WB QFN
Board
WCSP
Board
FCOL QFN
Board
Hotrod
Courtesy of ALPS

## Slide 5
LM53625 / LM53635 Viper Package
Package is 4mm x 5mm 22 pin QFN Flip Chip On Lead (HotRod) Technology.

## Slide 6
Wettable flanks
Wettable flanks guarantees visible side-wetting at good solder joints
Enables 100% Automotive Visual Inspection assembly processes
Dual plated punched process with notch on underside of the package.
Leadframe is punched out then re-plated.

## Slide 7: Images of QFN Slotted & Standard Leads
Slotted Leads – side view
Standard Leads – side view
Slotted Leads – Bottom view
Standard Leads – Bottom view
Plated Slot

## Slide 8: Wettable flanks with step-cut and re-plating
Step-cut

## Slide 9: Finished Product: Side Solder Fillet (SSF) on QFN
Standard QFN – poor solder fillet
Good Solder Fillet with step-cut wettable flanks

## Slide 10: Why do we need Automotive Hotrod?

## Slide 11: Why do we need Automotive Hotrod?
Reduced Rds_on
Smaller size
Reduced parasitics => less switch node ringing => lower EMI

## Slide 12
LM53625/35 Leadframe design
TI Confidential NDA Restrictions
0.6mm spacing between HV and LV pins
FB away from noisy signals and shielded by AGND
Note Symmetry for VIN/PGND around SW node
Wettable Flanks shown by notch

## Slide 13: Layout for EMI

## Slide 14: Which switch node am I?
QFN Wirebond
FCOL
FCOL
TSSOP Wirebond
LM53635
FCOL Hotrod

## Slide 15
Competitor
VIN=13.5, IOUT=3A
Measured with 10ns / div, 2V/div Ringing observed at about 200MHz
LM53635
VIN=13.5, IOUT=3A
Measured with 10ns / div, 2V/div
Minimal ringing
Not all switchers are equal: Switch Node Ringing

## Slide 16: Parallel input and output cap placement
Parallel capacitance loops minimize inductance
Minimizes switch node ringing
Minimizes output ripple
Make Mid-layer 1 as GND (keep close to top layer). Keep Mid-Layer1 GND intact underneath switch node

## Slide 17: 4 – Layer PCB EVM Stack-Up
Dielectric1
GND
LM53635x
Dielectric2
Core
GND
0.4 mil
2.8 mil
10mil
1.4 mil
32 mil
1.4 mil
10 mil
2.8 mil
0.4 mil
Top Solder
Top Layer1
Dielectric1
Mid Layer2
Dielectric3
Mid Layer3
Dielectric2
Bottom Layer4
Bottom Solder
Copper
2 oz.
1 oz.
1 oz.
2 oz.
SW
GND
Vias 8mil
GND

## Slide 18: AGND Layout to minimize noise coupling
Do not bridge AGND pin to PGND under the chip!
If possible, connect AGND with PGND after VCC and BIAS caps

## Slide 19: Thermals and layout

## Slide 20
Thermal performance
TI Confidential NDA Restrictions
Which Layout is better?
L
IC
Both boards measured at 13.5V VIN, 5V,3A VOUT

## Slide 21
Thermal performance
TI Confidential NDA Restrictions
L
IC
Both boards measured at 13.5V VIN, 5V,3A VOUT
Thermal “edges” caused by signal traces cutting top layer
Inductor hot. Not connected well to output copper

## Slide 22
Thermal layout
Place numerous vias under the package for thermal relief.
Vias are also placed around CIN and GND areas for further thermal relief

## Slide 23: Summary
Automotive Hotrod and Wettable Flanks
  Big performance advantages with EMI and Efficiency
  Qualified and ready to use!

## Slide 24: Thank you
Silicon Valley Analog - Performance Regulator Solutions
Perry Tsao – Systems and Applications Manager
perry,tsao@ti.com