## Slide 1: Load Share Control using the UCC29002
Colin Gillmor: colingillmor@ti.com
TI Information – Selective Disclosure

## Slide 2: Load Share Control using the UCC29002
Part 1: Parallel Operation
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 3: Parallel Operation: How is it done ?
Several Options exist
Operation in Current Limit
Droop Regulation with Vo Trimming
Master / Slave
Democratic Master / Slave –
  Loadshare Bus
  Using the UCC29002
“Power Module” = PSU
Multiple Power Modules feed a Single Load
TI Information – Selective Disclosure

## Slide 4: Load Sharing
Parallel Operation for N+1 redundancy –
Improved Reliability
Improved Lifetime
Longer mean time between failures
Improved system availability
Cooling
Losses distributed over a number of sources
Load may be too big for a single PSU
System expansion
Easy to add extra modules
“Power Module” = PSU
Multiple Power Modules feed a Single Load
TI Information – Selective Disclosure

## Slide 5: Load Sharing
Load-sharing is: Equal current in all Modules
IO1 = IO2 = IO3
Example: 60A Load, With Load-sharing
3 Modules in parallel, (each with ILIMIT = 33A)
60A = 20A + 20A + 20A
If a Module fails: 60A = 30A + 30A +0A – load is shared
IO = 10A (20A increases to 30A)
Example: 60A Load, Without Load-sharing
60A = 33A + 20A + 7A
33A = current limit, 7A = light load
If a Module fails: 60A = 33A + 27A – load is not shared
IO = 20A (7A to 27A)
Multiple Power Modules* feed a Single Load
TI Information – Selective Disclosure

## Slide 6: Load Regulation
6
Basic system has:
A Voltage Source VO
VL reduces as the load increases (Load Regulation)
TI Information – Selective Disclosure
Typical Load Regulation Spec
  140mV 0A to 100A (0.5%)
  1kW, 24Vout
Current Limit
Load regulation line
VL / IL

## Slide 7: Current Sharing, Two Sources
7
Both sources supply current into a single load
Current will not share equally
Load regulation lines differ (slope and offset)
Operating points differ, IO1 ≠ IO2
TI Information – Selective Disclosure
VO1 = VO2 = VL
How do we get IO1 = IO2 ?
Load regulation lines VO / IO
IO1 ≠ IO2
Load Reg =Slope
Vo at No Load = Offset
Extreme case:
One source goes into ILim
Other source supplies rest of current

## Slide 8: Current Sharing, Two Sources
8
Adjust the output voltage of the Modules
Current shares equally but only at one load
TI Information – Selective Disclosure
Trim VO1 or VO2 so that IO1 = IO2
Load regulation lines
VO / IO
IO1 = IO2

## Slide 9: Current Sharing, Two Sources
9
If Load changes
Current sharing is lost
Re-trim required
Open Loop system – no feedback
TI Information – Selective Disclosure
Currents at Lighter Load
Very Busy Hands !
When Load Changes
VL changes and IO1 ≠ IO2
Load regulation lines
VO / IO

## Slide 10: Current Sharing, Two Sources
10
Problems
Trimming works only at a single load
If the load changes then the operating point changes and the currents may not be the same
Re-Trimming necessary (or accept poor load-sharing)
TI Information – Selective Disclosure
Currents at Lighter Load
Very Busy Hands !
Re-Trim VO1 or VO2 so that IO1 = IO2
Load regulation lines
VO / IO

## Slide 11: Current Sharing, Two Sources
11
Solution
Need an automatic method
UC29002 and UCC29002/1
Use Remote Sensing lines to trim VO
TI Information – Selective Disclosure
UCC29002
  Continuous, Automatic Trimming
Matched Currents
at all Loads*
UCC29002
Load regulation lines
VO / IO

## Slide 12: Load Share Control using the UCC29002
Part 1: Parallel Operation, Load Regulation and Load Sharing
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 13: The UCC29002 - Concept
Each UCC29002 controls one Module
IDEM* signal generated on LS Bus by Master UCC29002 (Auto Selected)
Slaves adjust Modules so that IO = IDEM
UCC29002 uses IADJ to adjust VO
Current Sensing Resistors measure IO
Block Diagram
*Voltage on LS bus is a current demand signal
TI Information – Selective Disclosure

## Slide 14: The Modules
Modules must
Have Remote sense capability or Vo adjust terminal
Have Pre-biased load capability
Must be able to start-up when VLOAD is already present
Must not be able to sink current
ORing diode will prevent this
Use one load share controller per module
TI Information – Selective Disclosure

## Slide 15: Remote Sensing
Separate connection to the Load: S+ and S-
ISNS is zero
VS+ = VL : VS1 = 0V.
Load regulation point is at VL not VO
Module regulates voltage from S+ to S-
Compensates for voltage drops in REXT* on both Positive and Negative lines
ISNS = 0
Sensing on both Positive and Negative
Compensates for voltage drops in both lines
REXT* = PCB traces, Cables, Connectors etc
Vout Regulation point
TI Information – Selective Disclosure

## Slide 16: Load Share Control using the UCC29002
Part 1: Parallel Operation, Load Regulation and Load Sharing
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 17: IO Sensing and V+ Adjust
17
Add a Current Sense Resistor RCS
VRADJ = IADJ * RADJ
VL = VRADJ + VS+
Change IADJ to adjust VL
VL increases by V across RADJ
VL can increase only – trim up only
ADJ is a current sink
Current Sense Amplifier Output
CSO = LS Bus Voltage (Master controller)
CSO < LS Bus Voltage (Slave controller)
High Side Sensing is also possible
TI Information – Selective Disclosure
(EA+ = EA-)

## Slide 18: Master / Slave
18
TI Information – Selective Disclosure
The Master controller is the one where VCSO is highest
(equivalent to highest IO and V+).
The LS_Driver in the Master UCC29002 forward biases the diode so that:
VLS Bus = VCSO_Master and IADJ_Master = 0
Slaves use IADJ to force IO_Slave = IO_Master
Diodes reverse biased in Slave controllers:
VCSO_Slave < VLS Bus
Master/Slave role is dynamic, can change if Master fails for example

## Slide 19: Load Share Control using the UCC29002
Part 1: Parallel Operation, Load Regulation and Load Sharing
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 20: Designing with the UCC29002:
Design procedure is outlined in the data sheet
There is a MathCad calculator on the product page at http://www.ti.com/product/UCC29002/toolssoftware
TI Information – Selective Disclosure

## Slide 21: Typical Application
High Side Current Sensing
One UCC29002 is the Master and controls the voltage on the LS Bus
UCC29002 on Module with highest Vo becomes the Master controller. Master does not trim Vo of its module
Selection of Master is automatic and dynamic
Master role may move to other controllers in the system
  If: Module Vout shifts with temperature or ageing for example
Master sets the IDEM signal onto the LS Bus
The other UCC29002 become slaves
Slaves use ADJ pin to trim Vo
IO_Slave = IO_Master
TI Information – Selective Disclosure

## Slide 22: High Side or Low Side Current Sense
Current Sense can be High Side or Low Side
The EVM and the Ref Design use High Side sensing
PMP10099: – 12Vout
EVM: 1V < Vout < 15V
Normally Low side is a better choice.
Works for both low and high output voltage applications
Most customers use Low Side
During testing, it is easier to measure the voltage drop across the shunt resistor if it is on the low side.
I’d recommend Low Side sensing
High Side
Low Side
TI Information – Selective Disclosure

## Slide 23: Low Side Current Sense with V+ sensing only
There are voltage drops in the current sensing (RCS) and external PCB resistances (REXT) which means that VLS_M not necessarily equal to VLS_S
Usually the errors are small enough to ignore – next slide
TI Information – Selective Disclosure

## Slide 24: Low Side Current Sense with V+ sensing only
Voltage drops in the current sensing (RCS) and external PCB resistances (REXT)
means that VLS_M not necessarily equal to VLS_S
Usually the errors are small enough to ignore
The voltage drop from GND_M to GND_S is
Usually the gain is fairly high (80) and the imbalance is dominated by differences in RCS rather than in REXT
If RCS and REXT are identical then the current sharing will be affected only by differences in the UCC29002 current amplifier gain (AM and AS).

## Slide 25: UCC29002 or UCC29002/1
UCC29002 includes ‘Start-Up and Adjust Logic’ block
Disconnect Switch initially set to OPEN
IADJ is set to maximum until Io reaches 80% of level set by LS bus
Disconnect Switch is then closed
Faster start-up than UCC29002/1
Output voltage overshoots possible at start-up
UCC29002/1 has no ‘Start-up and Adjust Logic’ block
IADJ starts at zero (no adjustment of Vout)
Load Sharing established more slowly
Output voltage overshoots much less likely
The UCC29002/1 is a better choice for most applications
TI Information – Selective Disclosure
Notes: In the UCC39002 and UCC29002, during start-up, the load share driver amplifier is disabled by the disconnect switch and the adjust amplifier is forced to sink the maximum current through the adjust resistor. This operating mode ensures that the module controlled by the UCC39002 will be able to quickly engage in sharing the load
current since its output will be adjusted to a sufficiently high voltage immediately at turnon. Both the load share driver and the adjust amplifiers revert to normal operation as soon as the measured current exceeds 80% of the average per module current level represented by the LS bus voltage.
The UCC29002 and UCC29001 does not have this logic at start up. In this way, the UCC2900x does not adjust the output of the module to its maximum adjustment range at turn on and engages load sharing at more moderate rate.

## Slide 26: UCC29002/1 block Diagram
Current Sense Amplifier
Differential Amplifier
Minimum Gain = 3
Input is VCS
Output is A(VCS+VIO)
Low Offset is critical
VIO < ±100V
Disconnect Switch
Open if VCS+ ≈ 0.5V < VCS-
Closed otherwise
Load Share Bus Driver
LS = CSO in Master*
Output is Low in Slave (diode reverse biased)
Master controller is the one where VCSO is highest
The LS_Driver in Master forward biases the diode
The LS_Driver in Slave reverse biases the diode
Load Share Bus Receiver
Unity gain buffer for LS Bus
100kOhm loads LS Bus
ADJ Amp
Puts VEAO voltage across 500 
Sets IADJ = VEAO / 500 
Error Amp
Inputs: LS and CAO
Output controls IADJ
MOSFET
ON if VCS+ ≈ 0.5V < VCS-
Other Blocks
Enable
VDD Clamp
Fault
Logic
TI Information – Selective Disclosure

## Slide 27: VDD and ADJ pin
4.575V < VDD < 13.5 (15V AbsMax)
VEAO +1V < VADJ < VDD
FET protects ADJ pin from voltages > VDD
FET may not be needed if VDD < 13.5V BUT check for transient conditions at system turn-on and turn-off. Especially if VDD is from a separate supply
ADJ pin is a current sink
IADJ = ISNS + IR_ADJ
RINT appears in parallel with RADJ
Normally RINT >> RADJ
Note: sometimes diodes are used
TI Information – Selective Disclosure

## Slide 28: LS pin
LS
0 V < VLS < VDD – 1.7V
0 < ILS < -1mA
Internal 100 k to GND on each IC
Load on the LS bus is n x 100k in parallel
Limits the number of modules the device can control –
Load Share Amplifier is internally compensated (15kHz pole).
We recommend that the user does not put any filter capacitance on the LS line
Voltage on the Master LS pin is A * RCS * IO
A is the current amplifier gain
Voltage on Slave LS pin is approx the same
TI Information – Selective Disclosure

## Slide 29: Current Amplifier pins, CS+ and CS-
CS-, CS+
-0.3 V < VCS+ < VDD+0.3V
-0.3 V < VCS- < VDD+0.3V
Amplifier gain must be 3 or greater
Load Share controller will disconnect from the sharing system if VCS- is more than 500mV positive of VCS+
TI Information – Selective Disclosure

## Slide 30: Pin Voltage Limits:
CS-, CS+
-0.3 V < VCS+ < VDD+0.3V
-0.3 V < VCS- < VDD+0.3V
VDD
4.575V < VDD < 13.5V
Recommended range
CSO
-0.3 V < VCSO < VDD & < 11.8V
VCSO depends on gain and inputs
LS
0 V < VLS < VDD – 1.7V
0 < ILS < -1mA
100 k to GND
ADJ
VEAO+1V < VADJ < VDD
0 A < IADJ < 4.55mA
IADJ = VEAO / 500 
EAO
0V < VEAO < 3.5V
TI Information – Selective Disclosure
VADJ must NEVER exceed VDD
Vos can increase significantly
Turn-on and Turn-off

## Slide 31: Control Loop
31
TI Information – Selective Disclosure
There are two control loops:
Avoid interactions between loops:
Close the loop around the UCC29002 at least 1 decade below loop crossover of module
Load-Share loop is slow: may take 100ms to recover fully from a transient
RC at EAO sets UCC29002 bandwidth
Measure Loop bandwidth of Power Module
Ask Module manufacturer
Measure bandwidth (Bode Plot)
Estimate bandwidth from transient response
Composite response (Gtotal)
Module
UCC29002

## Slide 32: Load Share Control using the UCC29002
Part 1: Parallel Operation
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 33: UCC29002: Load Share Accuracy
33
TI Information – Selective Disclosure
RELATIVE Accuracy is the goal
Io_1 = Io_2 = Io_3 ….
Symmetrical layout
Vos of Current Amplifier < 100uV
VADJ must NEVER exceed VDD
  Vos can increase significantly and permanently
  Load Share accuracy will get worse.
  Turn-on and Turn-off
Relative Accuracy most important when Io is high
Module power is highest at high power
Relative Accuracy worse at lower currents (offsets)
Absolute currents are determined by the Load
Io_1 + Io_2 + Io_3 +….= I_Load
VERY, VERY important

## Slide 34: UCC29002: Other things to know
34
TI Information – Selective Disclosure
The UCC29002 is not a Hot-swap controller
Use products such as TPS23523 instead
To disconnect a module
Remove it from LS bus
Pull VCS- > 500mV positive of VCS+
Opens the disconnect switch
Fault Protection
Load Share bus short to GND
VDD Clamp
Clamp is a zener emulator
Needs 0.1uF < CVDD < 1uF for stability

## Slide 35: Load Share Control Current share resistor layout
35
TI Information – Selective Disclosure

## Slide 36: Load Share Control using the UCC29002
Part 1: Parallel Operation
Part 2: Introduction to the UCC29002
Part 3: How does the UCC29002 work
Part 4: Using the UCC29002
Differences between the UCC29002 and UCC29002/1
Part 5: Accuracy
Part 6: Typical Application
TI Information – Selective Disclosure

## Slide 37: PMP10099
37
TI Information – Selective Disclosure

## Slide 38: Load Share Control using the UCC29002
Thank you for your attention
Any Questions ?
Colin Gillmor: colingillmor@ti.com
TI Information – Selective Disclosure