## Slide 1: LM5025A Vs LM5027A Vs UCC2897A
Feature | LM5025A | LM5027A | UCC2897a | UCC2893
Internal Start-Up Bias Regulator | Yes 105V | Yes 105V | Yes, 110V | Yes, 110V
Main Gate Drive | 2A | 3A | 2A | 2A
Programmable (UVLO/OVLO) | UVLO | UVLO | UVLO & OVLO | UVLO & OVLO
Voltage Mode Control With Feedforward | Yes, | Yes | No | No
Current Mode Control | No | No | Yes | Yes
Dual Mode Overcurrent Protection | Yes, 500mV | Yes, 500mV | 500mV Cycle by Cycle, 750mV Hiccup | 750mV, Cycle by Cycle
SR Drive signal | No | Yes, Soft-start, soft stop | No | No
Programmable Time Delays Between Outputs | Yes | Yes | Yes | Yes
CS LEB | Yes | Yes | No | No
Cycle Current Limiting |  |  | Yes | Yes
Volt-second clamp | Yes | Yes | Yes | No
Programmable Soft Start | Yes | Yes | Yes | Yes
Max duty Cycle | 85% | 70% | 75% | 70%
Synchronisation | Yes | Yes | Yes | Yes
Maximum Frequency | 1MHz | 1MHz | 1MHz | 1MHz
Precision 5V reference | Yes | Yes | Yes | Yes
Thermal Shutdown | Yes | Yes | No | No

## Slide 2: LM5025 / A / B / C Active Clamp Controllers
The LM5025A, LM5025B and LM5025C are functional variants of the LM5025
HOME