## Slide 1: LM749x0-Q1 Power Mux Test Results
1st Feb, 2022
LP-PS

## Slide 2: Priority Power Mux Schematic

## Slide 3: Test Condition -1
HGATE and DGATE of AUX rail LM749x0-Q1 are enabled
when VPRIMARY drops below 9.2V
VOUT is powered from VPRIMARY
VOUT is powered from VAUX
VAUX starts supplying load
Test Condition:
Initial Condition:
  VPRIMARY =12V
  VAUX = 12V
Primary to Aux transition set at 9.2V
VPRIMARY drops below transition voltage
Observation:
As VPRIMARY drops below VOVF threshold, HGATE of AUX rail LM749x0-Q1 pulls high within 20us and starts powering the load

## Slide 4: Test Condition -1 Zoom in
Test Condition:
Initial Condition:
  VPRIMARY =12V
  VAUX = 12V
Primary to Aux transition set at 9.2V
VPRIMARY drops below transition voltage
Observation:
As VPRIMARY drops below VOVF threshold, HGATE of AUX rail LM749x0-Q1 pulls high within 20us and starts powering the load
HGATE of AUX rail LM749x0-Q1 turns ON within 20us
minimizing the VOUT voltage drop
VOUT is powered from VPRIMARY
VOUT is powered from VAUX
VAUX starts supplying load

## Slide 5: Test Condition -2
Test Condition:
Initial Condition:
  VAUX = 0V
  VPRIMARY =0V
VPRIMARY ramps up from 0V to 12V
Observation:
VOUT is powered from VPRIMARY
HGATE of PRIMARY path LM749x0-Q1 ramps up with inrush current control
VOUT is powered from VPRIMARY
VPRIMARY starts supplying load
HGATE of PRIMARY rail LM749x0-Q1 z
ramps up with dvdt control

## Slide 6: Test Condition -3
Test Condition:
Initial Condition:
  VAUX = 12V
  VPRIMARY =0V
VPRIMARY ramps up from 0V to 12V
Observation:
As VPRIMARY ramps up, VOUT is powered from VPRIMARY
HGATE of LM749x0-Q1 in AUX path is disabled when VPRIMARY ramps above VOVR threshold
VOUT is powered from VPRIMARY
VOUT is powered from VAUX
VPRIMARY starts supplying load
HGATE of AUX rail LM749x0-Q1 is disabled
when VPRIMARY goes above 10V