## Slide 1: LMG3100 SIMPLIS MODEL
User Guide

## Slide 2: Importing the Model
Include LMG3100R017_SIMPLIS_V1_5.sxcmp in the same folder as the schematic(.sxsch).
Goto: Place -> Hierarchy -> Component(Relative Path) and select the model .sxcmp file.
Place the model into your circuit. It will look like this.

## Slide 3: Using the Model
Make the circuit and use the required pins as recommended in the datasheet.
Use initial condition for HB-HS cap voltage and set it as 0V.
Simulate the circuit using appropriate analysis mode.
Example circuit – Buck Converter
BuckModel_LMG3100R017.sxsch is included for you reference.

## Slide 4: Questions
If you face any issue with the model, please contact – m-wagle@ti.com or gan_apps@ti.com