## Slide 1
Question - 1
Fuse
24VIN
Common Mode Filter
TPS2491
PGND
DGND
24VOUT
DGND
Current Connection
10.1.1 PC Board Guidelines (citation)
• The ground connection for the various components around the TPS2490 must be connected directly to each other and to the TPS2490's GND pin, and then connected to the system ground at one point. Do not connect the various component grounds to each other through the high current ground line.
According to the datasheet P.26 10.1.1 PC Board Guidelines, does the current connection comply with the description in the data sheet?
Fuse
24VIN
Common Mode Filter
TPS2491
PGND
24VOUT
PGND
DGND
Better?
PGND
Should it change to listed below?

## Slide 2
Fuse
24VIN
Common Mode Filter
TPS2491
PGND
DGND
24VOUT
DGND
current connection
Question - 2
Currently, the order of the components of the input is fuse, common mode filter, TPS2491.
In this case, the inrush current of the common mode filter can not be suppressed.
Fuse
24VIN
TPS2491
Commom Mode Filter
PGND
DGND
24VOUT
DGND
Idea 1
PGND？DGND？
Fuse
24VIN
TPS2491
Common Mode Filter
PGND
DGND
Idea 2
PGND
PGND？DGND？
Therefore, I want to order fuse, TPS 2491, common mode filter. Is there a problem?
In that case, which of the PGND and DGND will be the GND connecting the TPS 2491 and the common mode filter?
Furthermore, is there a problem with TPS 2491, fuse, common mode filter in order?
Which should be connected PGND or DGND?