## Slide 1
TPS54429
12V
5.5V
R:10kohm
R:1.6kohm
FET
Drain
Gate
Source
2.8V
Vout
2.8V
Discreate LDO
L
Why doesn’t drop to 0V the moment a short circuit occurs?
Short!!
From the moment the short circuit occur, the output voltage of DCDC gradually drops
And it take 330us to reach 0V. Why is that?
330us
Discreate LDO is very simple circuit
It does not have short circuit protection
If short is occurred on load of LDO, DCDC’s OCP will work.
2.8V
5.5V
GND

## Slide 2
We guess the UVP circuit worked is that correct?
65%
UVP delay counter is working
If short circuit occur until becomes 65%, we guess UVP circuit begins working.
You can check the details about that bellow comment.
Page 8 : Over/Under Voltage Protection
Link: https://www.ti.com/jp/lit/gpn/tps54429
------
“When the feedback voltage becomes
lower than 65% of the target voltage,
the UVP comparator output goes high
and an internal UVP delay counter begins.
After 250 µs, the device latches off
both internal top and bottom MOSFET. ”
--------