## Slide 1
LM74700
Dual Ideal Diode
Controller
DC-DC 24V
LM5143
Controller
DC-DC 12V
LM5144
Controller
TPS4811
Smart e-Fuse
Controller
G_LED
TPS4811
Smart e-Fuse
Controller
50.8V Battery
420W
60W
50.8V 35A bi-direction
MOSFET SMD
100V 100A (have heat sink)
MOSFET SMD
100V 100A (have heat sink)
MOSFET SMD
100V 100A (have heat sink)
OR
Alarm(OCP)
Multi-Phase
R_LED
G_LED
G_LED
25Apeak
14Apeak
G_LED
G_LED
Motor
Photo on/off
50.8V
Photo on/off
Photo on/off
14000uF
Inrush
Soft start
OCP/SCP
Motor
May Using Back to back method
Must be frequency synchronized (Sync) with 24V and 12V Controller

## Slide 2
Channel / Application | Load Specification | Key Technologies & Protection Requirements
Input (Battery Power / Charging) | 50.8V | Power input, requires reverse polarity protection.
Output (Motor) | 48V / 25Apeak | Must withstand a massive 14,000uF capacitive load. Requires soft start, short circuit, and overcurrent protection.
Output (Motor) | 48V / 14Apeak | Requires short circuit and overcurrent protection.
Output (System) | 12V / 60W | Eff(>88%)=90%,Ripple limited to 1%. Must be frequency synchronized (Sync) with the 24V output.
Output (System) | 24V / 420W | Eff(>88%)=90%,Ripple limited to 1%. Must be frequency synchronized (Sync) with the 12V output.