## Slide 1
Short
R1：47kΩ
R4：10kΩ
R8：1.6kΩ
C53：2200pF
OPEN
J9：To power
J14：To load
VIN
Measurement
point
VOUT
Measurement point
External SW
Customer changed some components on TPS25981EVM

## Slide 2
Vin: 5V, R_ILM:1.5kohm, ILIM:4.13A
ITIMER pin leave open
t_ITIMER: 14.2us
Question:
t_ITIMER is 14.2us when ITIMER pin open.
Is this result reasonable?

## Slide 3
Target slew rate: 1.5V/ms
From eq.4,
CdVdT(C53) :2200 pF
Result slew rate: 1.052 V/ms
Question:
Datasheet equation and results do not match.
Where are the factors?
Vin: 5V, R_ILM:1.5kohm, ILIM:4.13A

## Slide 4
Short VOUT with PGND
As a result,
Turn off current: 2.6A
Time to begin turn off: about 30ms
Vin: 5V, R_ILM:1.5kohm, ILIM:4.13A
Question:
When short, the current which turn off start is smaller than ILIM.
And high current continue 30ms.
Is this result reasonable?