## Slide 1
2017-03-30
Sanghee Byun / Advanced Research Team
Index
TPS54122 Test
EVM Setting
Resistor Setting
Test Setting
Test Result

## Slide 2: EVM Setting
1.
2.
3.
1. VIN - LDO IN Direct Connecting (VIN = 5V, JP2 : OFF)
2. JP4 : OFF, OFF-SW_EN Non Connecting
3. JP3 : VIN-LDO_BIAS Connecting
1.

## Slide 3: Resistor Setting
LDO OUT : 3.3V | 
R1 | R2
10K | 3.2K
SW OUT : 1.2V |  | 
R4 | R5 | R6
12.7K | 10K | 22.1K
1. SW OUT Resistor Set
2. LDO OUT Resistor Set

## Slide 4: Test Setting
VIN : 5V INPUT
0.1~3A Load
SW OUT
LDO OUT

## Slide 5: Test Result
Test – 8 : SW OUT
Test No. | Load Current (A) | SW OUT (V) | LDO OUT (V)
1 | No load | 3.3167 | 1.1959
2 | 0.1 | 3.2873 | 1.1929
3 | 0.5 | 3.2783 | 1.1803
4 | 1 | 3.2674 | 1.1647
5 | 1.5 | 3.2566 | 1.1494
6 | 2 | 3.2441 | 1.1341
7 | 2.5 | 3.2323 | 1.1186
8 | 3 | 3.218 | 1.1033
Test – 8 : LDO OUT