## Slide 1: TPS55288 Layout Review
09/03/2024

## Slide 2: Buck-leg MOSFETs
Put the MOSFETs more compacyt. PCB parasitic inductance could be reduced to minimum, which helps to improve SW1 pin spikes duing switching, as well as EMI performance.

## Slide 3: High-Side-FET Drive Traces Routing
To minimize gate-loop area, gate and source traces are routed side by side as differential pairs.

## Slide 4: AGND plane
It’s important to isolate the AGND plane and power ground plane. I am not sure but I think you use separate AGND here

## Slide 5: Vias
Put enough vias for thermal.