## Slide 1: TPS61094 Overview
APP/SR/BCC
Aug. 2025

## Slide 2
TPS61094 (Photon)
60-nA Iq bi-directional buck/boost converter with 4nA bypass mode
Benefits
Applications
Features
TPS61094
Input voltage range: 0.7V – 5.5V, startup 1.8V
Programmable boost output voltage, from 2.7V to 5.4V
Programmable buck output voltage, from 1.7V to 5.4V
Programmable buck output current, from 2.5mA to 600mA
Minimum 1.7A switch valley current limit
High efficiency: up to 96.3% efficiency at VIN = 3V, VOUT = 3.6V, and Iout = 100mA
Pin selectable buck/boost/bypass/true shurdown mode
  EN = 1, MODE = 1: Auto buck or boost mode
  EN = 1, MODE = 0: Forced buck mode
  EN = 0, MODE = 0: Forced bypass mode
  EN = 0, MODE = 1: True shutdown mode
Bypass mode with about 2nA Iq (typ)
Boost mode with about 60nA Iq (typ)
Buck mode with about 60nA Iq (typ)
Rdson: 60mΩ(LS),150mΩ (HS), 120mΩ Bypass switch
1 MHz switching frequency
±2% Reference voltage accuracy over -40℃ to +125℃
Output short protection
  2mm × 3mm 12-pin WSON package
  Gas meter, Water meters
  Energy Harvest
  60nA ultra low Iq: increase light load efficiency to extend battery run time.
  Bi-directional buck/boost is suitable for supercap backup power solution.
  Bypass switch: decrease power loss and high performance at load transient

## Slide 3: Super-capacitor Charger and Path Management for Backup Power Solution in E-meter
Boost
AC/DC
Buck
4G/2G
Power Mux
Charger
Charge / Discharger Control
AC/DC
Buck
4G/2G
TPS61094
Save from 3 devices to 1 device with charge/discharge control
Save from 5 power MOSFETs to 3 power MOSFETs by:
  Reusing the Boost power FETs as charger.
  Reusing the Boost high side FETs as one of power switch.
Traditional power architecture
New power architecture

## Slide 4: Existing device – TPS61094
Bi-direction LV buck and boost, optimized in Supercap Management

## Slide 5: Application Circuit: Pure Boost with Bypass
Vin > target Vout
Bypass mode
1
Vin < target Vout
Boost mode
2
BOOST
BYPASS
MODE=1 EN=1
MODE=1 EN=1

## Slide 6: Application Circuit: Boost with Buck Charger
Vin > target Vout+0.1V
Buck Charger
1
BYPASS
Vin < target Vout
Boost Converter
2
BUCK
Set Vout= 3.6V by R1
MODE=0 EN=1
Set supercap terminate voltage =2.6V by R3
BOOST
Set Vout= 3.6V by R1
Vout=3.6V
MODE=1 EN=1
Set supercap terminate voltage =2.6V by R3
X
EDLC
EDLC

## Slide 7: Application Example: Bypass Mode and Buck Charge Mode
When main power is present, and VOUT is not lower than 3.9V, super cap is charged in Buck mode.
1
4V ~ 3.9V
Set super-cap max charging current by R3.
Set super-cap terminate voltage by R4.
Buck Charge
Bypass
4V
ICHG is set at 500mA
VCHG is set at 2.1V
0V

## Slide 8: Application Example: Bypass Mode (charge disable)
When main power is present, and super-cap is charged to VCHG, charge mode is disbaled, only bypass FET is turned on.
Status pin is pulled high.
2
4V ~ 3.9V
Bypass
4V
2.1V
Status pin is pulled high when charging down.

## Slide 9: Application Example: Boost Discharge Mode
When main power is not present, supercap is discharged to power for loads.
3.9V
Boost Discharge Mode
Set output voltage in Boost mode by R1， R2
3
VOUT_SET in boost mode is set at 3.9V

## Slide 10: Operation Mode
Mode | EN | MODE | Function
Ture shutdown | 0 | 0 | Ture shutdown mode. Bypass disconnect. VOUT = 0V
Forced bypass mode | 0 | 1 | Force bypass mode. VOUT = VIN
Forced buck charge mode | 1 | 0 | Force buck charge mode. Bypass MOS turns on(VOUT = VIN) while charging the supercap or backup battery
Auto charging or backup | 1 | 1 | When VIN >= VOUT & VOUT >= VOUT_SET + 0.1V, then Charging function enable, turn on Buck, Supercap is charged by buck.
 | 1 | 1 | When VIN >= VOUT & VOUT_SET + 0.1V > VOUT >= VOUT_SET, then Charging function disable, only bypass FET is turned on.
 | 1 | 1 | When VIN < VOUT & VOUT < VOUT_SET, then Backup function enable, turn on Boost, VOUT is powered by Supercap.