## Slide 1
CH1(BAT current), CH2(VBAT), CH2(PMID), CH4(VSYS)
. TA : Samsung EP-TA50KWK 001. Output(5V 1.55A)
. - Battery Pack : Li-ion 4s1p, Fast Charging (0.5C), Discharging current (1C typ, 2c max)
Output Voltage (14.4V typ), Charging Voltage(16.8V)
Cutoff discharging voltage(11.2V), Recover Voltage(12V)
150Sec
220Sec
1210Sec
1240Sec
1320Sec
1. Charging issue of BQ25798 ( PBA#13 ). 20240701 Report
220Sec
around 1200Sec
around 1230Sec
around 1320Sec
1). Issue and Symtom : During charging, the current increases and then Stop the fast charging.
ⓐ Charging start : CE High to Low. Charging status of Register is indicate Fast charging.
ⓒ Charging Current was ramp-up rapidly(around 2.3mA) at battery voltage 15~15.1V after that, stop Fast charging. Issue to Focus on.
( refer to below figure1 of page 1)
2) Requtst: Please give me advice on solving problems in circuit or PCB design.

## Slide 2
1. Charging issue of BQ25798 ( PBA#12 ). 20240701 Report
1). Issue and Symtom : During charging, the current increases and then Stop the fast charging.
ⓐ Charging start : CE High to Low. Charging status of Register is indicate Fast charging.
ⓑ IBAT register shows always 0mA ( after set 80h of Index 2Eh ), but low current charging is continuing.
ⓒ Charging Current was ramp-up rapidly(around 2.3mA) at battery voltage 15~15.1V after that, stop Fast charging
( refer to below figure1 of page 1)
2) Test enviroment
- Battery Pack : Li-ion 4s1p, Fast Charging (0.5C), Discharging current (1C typ, 2c max)
Output Voltage (14.4V typ), Charging Voltage(16.8V)
Cutoff discharging voltage(11.2V), Recover Voltage(12V)
3) Requtst: Please give me advice on solving problems in circuit or PCB design.
※ Figure 1
CH1(BAT current), CH2(VBAT), CH2(VBUS), CH4(VSYS)
※ Please note that the oscilloscope's measured waveform values ​​have high deviation. Looking at the dumped register value, it is VSYS≥VBAT.